Profiling x264- To identify the cycle-intensive modules(mostly used cpu cycle by which model

 the four modules: Intra Prediction, Transform, Entropy Coding, and Motion Estimation.

Ffmpeg -i input.y4m

Format: yuv4mpegpipe — indicates a YUV4MPEG2 format.
- Duration: 00:00:10.01 — about 10 seconds.
- Bitrate: 36460 kb/s — high raw data rate (typical for uncompressed YUV).
- Codec: rawvideo (I420) — raw uncompressed video using I420 (YUV 4:2:0).
- Pixel format: yuv420p(progressive) — standard 4:2:0 planar format.
- Resolution: 352x288 — standard CIF (Common Intermediate Format).
- SAR: 128:117 — Sample Aspect Ratio (each pixel is slightly taller than wide).
- DAR: 1408:1053 — Display Aspect Ratio, determines overall frame shape.
- Framerate: 29.97 fps — NTSC-compatible framerate.

./x264 --preset medium --crf 23 --output output.h264 input.y4m

--preset medium: A balanced trade-off between speed and compression.
--crf 23: Constant Rate Factor for quality control (lower = better quality; 18–28 typical range).
--output output.h264: Encoded output file.
input.y4m: YUV4MPEG2 raw video input file.
----------------------------------------------------------------------------------------------------------------------------
encoded
mirafra@mirafra:~/x264$ ./x264 --preset medium --crf 23 --output output.h264 input.y4m
y4m [info]: 352x288p 128:117 @ 30000/1001 fps (cfr)
x264 [info]: using SAR=128/117
x264 [info]: using cpu capabilities: MMX2 SSE2Fast SSSE3 SSE4.2 AVX FMA3 BMI2 AVX2 AVX512
x264 [info]: profile High, level 1.3, 4:2:0, 8-bit
x264 [info]: frame I:2 Avg QP:18.16 size: 13905
x264 [info]: frame P:76 Avg QP:22.34 size: 1108
x264 [info]: frame B:222 Avg QP:29.15 size: 107
x264 [info]: consecutive B-frames: 1.0% 0.7% 1.0% 97.3%
x264 [info]: mb I I16..4: 6.6% 65.0% 28.4%
x264 [info]: mb P I16..4: 0.0% 0.1% 0.0% P16..4: 15.7% 9.9% 7.2% 0.0% 0.0% skip:67.0%
x264 [info]: mb B I16..4: 0.0% 0.0% 0.0% B16..8: 12.9% 1.1% 0.2% direct: 0.2% skip:85.7% L0:35.0% L1:57.7% BI: 7.3%
x264 [info]: 8x8 transform intra:65.0% inter:51.2%
x264 [info]: coded y,uvDC,uvAC intra: 91.8% 91.3% 77.2% inter: 3.1% 2.3% 0.4%
x264 [info]: i16 v,h,dc,p: 63% 12% 4% 21%
x264 [info]: i8 v,h,dc,ddl,ddr,vr,hd,vl,hu: 24% 27% 16% 4% 5% 7% 5% 6% 6%
x264 [info]: i4 v,h,dc,ddl,ddr,vr,hd,vl,hu: 31% 10% 10% 6% 7% 12% 6% 12% 6%
x264 [info]: i8c dc,h,v,p: 40% 24% 27% 9%
x264 [info]: Weighted P-Frames: Y:0.0% UV:0.0%
x264 [info]: ref P L0: 62.2% 16.1% 14.3% 7.5%
x264 [info]: ref B L0: 91.8% 6.2% 2.0%
x264 [info]: ref B L1: 95.9% 4.1%
x264 [info]: kb/s:108.45

---------------------------------------------------------------------------------------------------
Output Analysis
#### 🔹 General Info
- Resolution: 352x288
- SAR (Sample Aspect Ratio): 128:117
- Frame Rate: 30000/1001 ≈ 29.97 fps
- Profile: High (better compression & quality than baseline/main)
- Level: 1.3 (suitable for low-res, low-bitrate content)
- Chroma Subsampling: 4:2:0
- Bit Depth: 8-bit
- CPU Features Used: AVX, AVX2, AVX512, etc.
#### 🔹 Frame Stats
- I-Frames: 2 (Intra-coded, highest quality) — large size
- P-Frames: 76 (Predicted) — moderate size
- B-Frames: 222 (Bidirectional) — smallest size, most frequent
- Consecutive B-frames: Mostly 3 in a row (97.3%)
#### 🔹 Macroblock (mb) Usage
Shows how different prediction and transform modes are used, e.g.:
- skip: 67% in P-frames — indicates efficient compression
- i16, i4, i8: intra prediction types
#### 🔹 Transform Analysis
8x8 transform usage: intra 65.0%, inter 51.2% — more efficient for compression.
#### 🔹 Reference Frames
- Ref P L0: Shows how often previous frames were used for prediction in P-frames.
- Ref B L0/L1: Similar stats for B-frames.
#### 🔹 Final Bitrate
kb/s: 108.45 — relatively low bitrate (low-resolution test clip).
#### 🔹 Encoding Speed
1505.83 fps — very fast encoding, likely due to low resolution and powerful CPU.

------------------------------------------------------------------------------------------------------------------------Frame by frame encoding
10 sec video =29 fps=299 frames
each frame encoded how
----------------------------------------------------------------------------------------------------------------

Lower QP values (e.g., 0–20) result in less quantization, preserving more detail and yielding higher quality but larger file sizes.
Higher QP values (e.g., 30–51) result in more aggressive quantization, discarding more detail, leading to lower quality but smaller file sizes.
NAL Units:
The Network Abstraction Layer (NAL) is a key component of the H.264 standard designed to structure and package compressed video data for storage or transmission. The NAL separates the video coding layer (VCL), which handles the core compression of video frames, from the transport layer, which ensures the data can be efficiently delivered over various networks or stored in files.
Purpose of NAL:
- Modularity: NAL units encapsulate different types of data (e.g., video frames, metadata, or configuration) into self-contained packets, making it easier to handle the bitstream in diverse environments (e.g., streaming, broadcasting, or file storage).
- Network Friendliness: NAL units are designed to be transmitted over packet-based networks (e.g., IP networks) or stored in formats like MP4 or MKV, with each unit being independently decodable to some extent.
- Flexibility: NAL units allow the encoder to include both video data (e.g., encoded frames) and non-video data (e.g., sequence parameters) in the same bitstream.
NAL Unit Structure:
- Each NAL unit consists of a header and a payload.
- The NAL unit header is typically 1 byte (or more in some cases) and contains:
  - Forbidden Zero Bit (1 bit): Must be 0; used to detect bitstream errors.
  - NAL Reference IDC (nal_ref_idc) (2 bits): Indicates the importance of the NAL unit (e.g., whether it’s a reference frame or disposable).
  - NAL Unit Type (nal_unit_type) (5 bits): Specifies the type of data in the payload (e.g., a slice of a frame, parameter set, etc.).
- The payload contains the actual data, such as encoded video slices, sequence parameter sets (SPS), or picture parameter sets (PPS).
NAL Unit Types: The H.264 standard defines various NAL unit types, each serving a specific purpose. The nal_unit_type is a 5-bit value (0–31), with common types including:
- 1: Coded slice of a non-IDR picture (e.g., P or B frame).
- 2: Coded slice data partition A (used in data partitioning, rare). Contains the slice header and critical data like macroblock types, motion vectors, and intra-prediction modes.
- 3: Coded slice data partition B (rare). Contains intra-coded macroblock residual data.
- 4: Coded slice data partition C (rare). Contains inter-coded macroblock residual data.(a keyframe that resets the decoder state).
- 5: Coded slice of an IDR picture (keyframe).
- 6: Supplemental Enhancement Information (SEI).
- 7: Sequence Parameter Set (SPS).
- 8: Picture Parameter Set (PPS).
- 9: Access Unit Delimiter (AUD).
- ... and others for specific purposes.
Poc:4:
PoC stands for Picture Order Count. It represents the display order of the frame in the video sequence. Here, PoC=4 means this frame is intended to be displayed as the fourth frame in the output, which may differ from the encoding order due to B-frames (which can be encoded out of order).
I:0:
Indicates the number of I-macroblocks (Intra-coded macroblocks) in the frame. I-macroblocks are encoded without reference to other frames. Here, I:0 means there are no Intra-coded macroblocks in this B-frame, which is typical since B-frames rely on prediction.
P:47:
Indicates the number of P-macroblocks (Predicted macroblocks) in the frame. P-macroblocks are predicted from previous frames. Here, P:47 means 47 macroblocks in this frame are predicted using motion compensation from reference frames.
SKIP:349:
Indicates the number of skipped macroblocks. Skipped macroblocks are not encoded explicitly because they are deemed similar enough to their reference (from other frames) that no additional data is needed. Here, SKIP:349 means 349 macroblocks were skipped, which is common in B-frames for areas with little or no change, improving compression efficiency.

-----------------------------------------------------------------------------------------------------------------------
mirafra@mirafra:~/x264$ ./x264 --log-level debug --preset medium --crf 23 --output output.h264 input.y4m
y4m [info]: 352x288p 128:117 @ 30000/1001 fps (cfr)
x264 [debug]: using mv_range_thread = 24
x264 [info]: using SAR=128/117
x264 [info]: using cpu capabilities: MMX2 SSE2Fast SSSE3 SSE4.2 AVX FMA3 BMI2 AVX2 AVX512
x264 [info]: profile High, level 1.3, 4:2:0, 8-bit
x264 [debug]: frame= 0 QP=19.57 NAL=3 Slice:I Poc:0 I:396 P:0 SKIP:0 size=11924 bytes
x264 [debug]: frame= 1 QP=20.79 NAL=2 Slice:P Poc:8 I:0 P:93 SKIP:303 size=485 bytes
x264 [debug]: frame= 2 QP=27.00 NAL=2 Slice:B Poc:4 I:0 P:47 SKIP:349 size=52 bytes
x264 [debug]: frame= 3 QP=28.00 NAL=0 Slice:B Poc:2 I:0 P:25 SKIP:371 size=39 bytes
x264 [debug]: frame= 4 QP=30.55 NAL=0 Slice:B Poc:6 I:0 P:12 SKIP:384 size=32 bytes
x264 [debug]: frame= 5 QP=21.37 NAL=2 Slice:P Poc:16 I:0 P:89 SKIP:307 size=416 bytes
x264 [debug]: frame= 6 QP=28.77 NAL=2 Slice:B Poc:12 I:0 P:38 SKIP:358 size=121 bytes
x264 [debug]: frame= 7 QP=28.00 NAL=0 Slice:B Poc:10 I:0 P:25 SKIP:371 size=41 bytes
x264 [debug]: frame= 8 QP=30.94 NAL=0 Slice:B Poc:14 I:0 P:14 SKIP:382 size=55 bytes
x264 [debug]: frame= 9 QP=21.48 NAL=2 Slice:P Poc:24 I:1 P:111 SKIP:284 size=862 bytes
x264 [debug]: frame= 10 QP=28.91 NAL=2 Slice:B Poc:20 I:0 P:44 SKIP:352 size=109 bytes
x264 [debug]: frame= 11 QP=28.00 NAL=0 Slice:B Poc:18 I:0 P:25 SKIP:371 size=45 bytes
x264 [debug]: frame= 12 QP=29.90 NAL=0 Slice:B Poc:22 I:0 P:20 SKIP:376 size=47 bytes
x264 [debug]: frame= 13 QP=21.76 NAL=2 Slice:P Poc:32 I:0 P:156 SKIP:240 size=1106 bytes
x264 [debug]: frame= 14 QP=28.91 NAL=2 Slice:B Poc:28 I:0 P:98 SKIP:298 size=165 bytes
x264 [debug]: frame= 15 QP=28.00 NAL=0 Slice:B Poc:26 I:0 P:54 SKIP:342 size=59 bytes
x264 [debug]: frame= 16 QP=29.90 NAL=0 Slice:B Poc:30 I:0 P:61 SKIP:335 size=97 bytes
x264 [debug]: frame= 17 QP=21.44 NAL=2 Slice:P Poc:40 I:0 P:180 SKIP:216 size=1740 bytes
x264 [debug]: frame= 18 QP=28.97 NAL=2 Slice:B Poc:36 I:0 P:114 SKIP:282 size=222 bytes
x264 [debug]: frame= 19 QP=28.00 NAL=0 Slice:B Poc:34 I:0 P:79 SKIP:317 size=106 bytes
x264 [debug]: frame= 20 QP=29.90 NAL=0 Slice:B Poc:38 I:0 P:92 SKIP:304 size=104 bytes
x264 [debug]: frame= 21 QP=21.87 NAL=2 Slice:P Poc:48 I:0 P:167 SKIP:229 size=1329 bytes
x264 [debug]: frame= 22 QP=27.69 NAL=2 Slice:B Poc:44 I:0 P:96 SKIP:300 size=128 bytes
x264 [debug]: frame= 23 QP=28.00 NAL=0 Slice:B Poc:42 I:0 P:67 SKIP:329 size=74 bytes
x264 [debug]: frame= 24 QP=30.55 NAL=0 Slice:B Poc:46 I:0 P:70 SKIP:326 size=79 bytes
x264 [debug]: frame= 25 QP=21.15 NAL=2 Slice:P Poc:56 I:0 P:179 SKIP:217 size=1499 bytes
x264 [debug]: frame= 26 QP=29.31 NAL=2 Slice:B Poc:52 I:0 P:75 SKIP:321 size=188 bytes
x264 [debug]: frame= 27 QP=28.00 NAL=0 Slice:B Poc:50 I:0 P:58 SKIP:338 size=80 bytes
x264 [debug]: frame= 28 QP=29.76 NAL=0 Slice:B Poc:54 I:0 P:66 SKIP:330 size=107 bytes
x264 [debug]: frame= 29 QP=22.27 NAL=2 Slice:P Poc:64 I:0 P:169 SKIP:227 size=1542 bytes
x264 [debug]: frame= 30 QP=29.03 NAL=2 Slice:B Poc:60 I:0 P:114 SKIP:282 size=226 bytes
x264 [debug]: frame= 31 QP=28.67 NAL=0 Slice:B Poc:58 I:0 P:65 SKIP:331 size=112 bytes
x264 [debug]: frame= 32 QP=29.68 NAL=0 Slice:B Poc:62 I:0 P:66 SKIP:330 size=92 bytes
x264 [debug]: frame= 33 QP=21.79 NAL=2 Slice:P Poc:72 I:1 P:167 SKIP:228 size=1586 bytes
x264 [debug]: frame= 34 QP=28.88 NAL=2 Slice:B Poc:68 I:0 P:88 SKIP:308 size=209 bytes
x264 [debug]: frame= 35 QP=29.67 NAL=0 Slice:B Poc:66 I:0 P:64 SKIP:332 size=82 bytes
x264 [debug]: frame= 36 QP=30.94 NAL=0 Slice:B Poc:70 I:0 P:80 SKIP:316 size=124 bytes
x264 [debug]: frame= 37 QP=20.81 NAL=2 Slice:P Poc:80 I:1 P:166 SKIP:229 size=1953 bytes
x264 [debug]: frame= 38 QP=29.12 NAL=2 Slice:B Poc:76 I:0 P:105 SKIP:291 size=273 bytes
x264 [debug]: frame= 39 QP=31.44 NAL=0 Slice:B Poc:74 I:0 P:75 SKIP:321 size=181 bytes
x264 [debug]: frame= 40 QP=29.68 NAL=0 Slice:B Poc:78 I:0 P:84 SKIP:312 size=104 bytes
x264 [debug]: frame= 41 QP=21.74 NAL=2 Slice:P Poc:88 I:0 P:146 SKIP:250 size=1195 bytes
x264 [debug]: frame= 42 QP=29.14 NAL=2 Slice:B Poc:84 I:0 P:79 SKIP:317 size=120 bytes
x264 [debug]: frame= 43 QP=29.67 NAL=0 Slice:B Poc:82 I:0 P:62 SKIP:334 size=80 bytes
x264 [debug]: frame= 44 QP=28.00 NAL=0 Slice:B Poc:86 I:0 P:48 SKIP:348 size=63 bytes
x264 [debug]: frame= 45 QP=22.19 NAL=2 Slice:P Poc:96 I:0 P:150 SKIP:246 size=1310 bytes
x264 [debug]: frame= 46 QP=29.42 NAL=2 Slice:B Poc:92 I:0 P:76 SKIP:320 size=126 bytes
x264 [debug]: frame= 47 QP=28.00 NAL=0 Slice:B Poc:90 I:0 P:65 SKIP:331 size=74 bytes
x264 [debug]: frame= 48 QP=28.59 NAL=0 Slice:B Poc:94 I:0 P:52 SKIP:344 size=80 bytes
x264 [debug]: frame= 49 QP=22.11 NAL=2 Slice:P Poc:104 I:0 P:116 SKIP:280 size=630 bytes
x264 [debug]: frame= 50 QP=28.44 NAL=2 Slice:B Poc:100 I:0 P:68 SKIP:328 size=98 bytes
x264 [debug]: frame= 51 QP=28.00 NAL=0 Slice:B Poc:98 I:0 P:45 SKIP:351 size=55 bytes
x264 [debug]: frame= 52 QP=28.00 NAL=0 Slice:B Poc:102 I:0 P:31 SKIP:365 size=49 bytes
x264 [debug]: frame= 53 QP=23.04 NAL=2 Slice:P Poc:112 I:1 P:131 SKIP:264 size=962 bytes
x264 [debug]: frame= 54 QP=28.68 NAL=2 Slice:B Poc:108 I:0 P:65 SKIP:331 size=139 bytes
x264 [debug]: frame= 55 QP=29.68 NAL=0 Slice:B Poc:106 I:0 P:48 SKIP:348 size=82 bytes
x264 [debug]: frame= 56 QP=30.61 NAL=0 Slice:B Poc:110 I:0 P:32 SKIP:364 size=57 bytes
x264 [debug]: frame= 57 QP=22.67 NAL=2 Slice:P Poc:120 I:0 P:153 SKIP:243 size=902 bytes
x264 [debug]: frame= 58 QP=29.22 NAL=2 Slice:B Poc:116 I:0 P:82 SKIP:314 size=153 bytes
x264 [debug]: frame= 59 QP=28.00 NAL=0 Slice:B Poc:114 I:0 P:57 SKIP:339 size=66 bytes
x264 [debug]: frame= 60 QP=29.95 NAL=0 Slice:B Poc:118 I:0 P:73 SKIP:323 size=118 bytes
x264 [debug]: frame= 61 QP=22.71 NAL=2 Slice:P Poc:128 I:0 P:152 SKIP:244 size=1346 bytes
x264 [debug]: frame= 62 QP=28.17 NAL=2 Slice:B Poc:124 I:0 P:90 SKIP:306 size=194 bytes
x264 [debug]: frame= 63 QP=30.69 NAL=0 Slice:B Poc:122 I:0 P:48 SKIP:348 size=80 bytes
x264 [debug]: frame= 64 QP=30.66 NAL=0 Slice:B Poc:126 I:0 P:49 SKIP:347 size=69 bytes
x264 [debug]: frame= 65 QP=21.53 NAL=2 Slice:P Poc:136 I:0 P:156 SKIP:240 size=1380 bytes
x264 [debug]: frame= 66 QP=29.27 NAL=2 Slice:B Poc:132 I:0 P:72 SKIP:324 size=238 bytes
x264 [debug]: frame= 67 QP=29.68 NAL=0 Slice:B Poc:130 I:0 P:65 SKIP:331 size=93 bytes
x264 [debug]: frame= 68 QP=30.61 NAL=0 Slice:B Poc:134 I:0 P:63 SKIP:333 size=115 bytes
x264 [debug]: frame= 69 QP=21.99 NAL=2 Slice:P Poc:144 I:1 P:165 SKIP:230 size=1935 bytes
x264 [debug]: frame= 70 QP=27.00 NAL=2 Slice:B Poc:140 I:0 P:87 SKIP:309 size=267 bytes
x264 [debug]: frame= 71 QP=30.32 NAL=0 Slice:B Poc:138 I:0 P:53 SKIP:343 size=103 bytes
x264 [debug]: frame= 72 QP=30.61 NAL=0 Slice:B Poc:142 I:0 P:67 SKIP:329 size=155 bytes
x264 [debug]: frame= 73 QP=21.77 NAL=2 Slice:P Poc:152 I:0 P:139 SKIP:257 size=1018 bytes
x264 [debug]: frame= 74 QP=28.35 NAL=2 Slice:B Poc:148 I:0 P:84 SKIP:312 size=264 bytes
x264 [debug]: frame= 75 QP=30.37 NAL=0 Slice:B Poc:146 I:0 P:54 SKIP:342 size=79 bytes
x264 [debug]: frame= 76 QP=30.37 NAL=0 Slice:B Poc:150 I:0 P:44 SKIP:352 size=81 bytes
x264 [debug]: frame= 77 QP=21.46 NAL=2 Slice:P Poc:160 I:4 P:154 SKIP:238 size=2095 bytes
x264 [debug]: frame= 78 QP=27.57 NAL=2 Slice:B Poc:156 I:0 P:80 SKIP:316 size=311 bytes
x264 [debug]: frame= 79 QP=30.35 NAL=0 Slice:B Poc:154 I:0 P:73 SKIP:323 size=160 bytes
x264 [debug]: frame= 80 QP=30.87 NAL=0 Slice:B Poc:158 I:0 P:55 SKIP:341 size=118 bytes
x264 [debug]: frame= 81 QP=21.96 NAL=2 Slice:P Poc:168 I:0 P:148 SKIP:248 size=1366 bytes
x264 [debug]: frame= 82 QP=28.97 NAL=2 Slice:B Poc:164 I:0 P:85 SKIP:311 size=186 bytes
x264 [debug]: frame= 83 QP=29.88 NAL=0 Slice:B Poc:162 I:0 P:50 SKIP:346 size=89 bytes
x264 [debug]: frame= 84 QP=30.12 NAL=0 Slice:B Poc:166 I:0 P:58 SKIP:338 size=81 bytes
x264 [debug]: frame= 85 QP=21.92 NAL=2 Slice:P Poc:176 I:1 P:162 SKIP:233 size=1327 bytes
x264 [debug]: frame= 86 QP=26.24 NAL=2 Slice:B Poc:172 I:0 P:96 SKIP:300 size=160 bytes
x264 [debug]: frame= 87 QP=29.79 NAL=0 Slice:B Poc:170 I:0 P:71 SKIP:325 size=115 bytes
x264 [debug]: frame= 88 QP=28.00 NAL=0 Slice:B Poc:174 I:0 P:60 SKIP:336 size=70 bytes
x264 [debug]: frame= 89 QP=21.28 NAL=2 Slice:P Poc:184 I:0 P:166 SKIP:230 size=1532 bytes
x264 [debug]: frame= 90 QP=29.36 NAL=2 Slice:B Poc:180 I:0 P:100 SKIP:296 size=162 bytes
x264 [debug]: frame= 91 QP=28.00 NAL=0 Slice:B Poc:178 I:0 P:66 SKIP:330 size=79 bytes
x264 [debug]: frame= 92 QP=28.00 NAL=0 Slice:B Poc:182 I:0 P:49 SKIP:347 size=66 bytes
x264 [debug]: frame= 93 QP=21.34 NAL=2 Slice:P Poc:192 I:0 P:169 SKIP:227 size=1525 bytes
x264 [debug]: frame= 94 QP=29.68 NAL=2 Slice:B Poc:188 I:0 P:92 SKIP:304 size=150 bytes
x264 [debug]: frame= 95 QP=28.00 NAL=0 Slice:B Poc:186 I:0 P:54 SKIP:342 size=69 bytes
x264 [debug]: frame= 96 QP=29.16 NAL=0 Slice:B Poc:190 I:0 P:60 SKIP:336 size=75 bytes
x264 [debug]: frame= 97 QP=20.89 NAL=2 Slice:P Poc:200 I:1 P:155 SKIP:240 size=910 bytes
x264 [debug]: frame= 98 QP=28.93 NAL=2 Slice:B Poc:196 I:0 P:77 SKIP:319 size=89 bytes
x264 [debug]: frame= 99 QP=27.05 NAL=0 Slice:B Poc:194 I:0 P:48 SKIP:348 size=61 bytes
x264 [debug]: frame= 100 QP=28.00 NAL=0 Slice:B Poc:198 I:0 P:44 SKIP:352 size=46 bytes
x264 [debug]: frame= 101 QP=21.28 NAL=2 Slice:P Poc:208 I:0 P:138 SKIP:258 size=1197 bytes
x264 [debug]: frame= 102 QP=26.95 NAL=2 Slice:B Poc:204 I:0 P:88 SKIP:308 size=156 bytes
x264 [debug]: frame= 103 QP=28.00 NAL=0 Slice:B Poc:202 I:0 P:42 SKIP:354 size=56 bytes
x264 [debug]: frame= 104 QP=29.68 NAL=0 Slice:B Poc:206 I:0 P:43 SKIP:353 size=84 bytes
x264 [debug]: frame= 105 QP=21.89 NAL=2 Slice:P Poc:216 I:1 P:155 SKIP:240 size=1571 bytes
x264 [debug]: frame= 106 QP=28.10 NAL=2 Slice:B Poc:212 I:0 P:89 SKIP:307 size=180 bytes
x264 [debug]: frame= 107 QP=29.68 NAL=0 Slice:B Poc:210 I:0 P:69 SKIP:327 size=120 bytes
x264 [debug]: frame= 108 QP=28.83 NAL=0 Slice:B Poc:214 I:0 P:75 SKIP:321 size=89 bytes
x264 [debug]: frame= 109 QP=21.04 NAL=2 Slice:P Poc:224 I:0 P:160 SKIP:236 size=1416 bytes
x264 [debug]: frame= 110 QP=28.86 NAL=2 Slice:B Poc:220 I:0 P:79 SKIP:317 size=141 bytes
x264 [debug]: frame= 111 QP=30.61 NAL=0 Slice:B Poc:218 I:0 P:60 SKIP:336 size=77 bytes
x264 [debug]: frame= 112 QP=28.00 NAL=0 Slice:B Poc:222 I:0 P:55 SKIP:341 size=65 bytes
x264 [debug]: frame= 113 QP=21.34 NAL=2 Slice:P Poc:232 I:0 P:141 SKIP:255 size=912 bytes
x264 [debug]: frame= 114 QP=28.37 NAL=2 Slice:B Poc:228 I:0 P:80 SKIP:316 size=109 bytes
x264 [debug]: frame= 115 QP=28.00 NAL=0 Slice:B Poc:226 I:0 P:47 SKIP:349 size=64 bytes
x264 [debug]: frame= 116 QP=28.00 NAL=0 Slice:B Poc:230 I:0 P:33 SKIP:363 size=54 bytes
x264 [debug]: frame= 117 QP=20.86 NAL=2 Slice:P Poc:240 I:0 P:110 SKIP:286 size=662 bytes
x264 [debug]: frame= 118 QP=26.99 NAL=2 Slice:B Poc:236 I:0 P:52 SKIP:344 size=88 bytes
x264 [debug]: frame= 119 QP=28.00 NAL=0 Slice:B Poc:234 I:0 P:30 SKIP:366 size=45 bytes
x264 [debug]: frame= 120 QP=28.00 NAL=0 Slice:B Poc:238 I:0 P:15 SKIP:381 size=31 bytes
x264 [debug]: frame= 121 QP=22.13 NAL=2 Slice:P Poc:248 I:0 P:121 SKIP:275 size=808 bytes
x264 [debug]: frame= 122 QP=28.68 NAL=2 Slice:B Poc:244 I:0 P:59 SKIP:337 size=99 bytes
x264 [debug]: frame= 123 QP=29.68 NAL=0 Slice:B Poc:242 I:0 P:37 SKIP:359 size=81 bytes
x264 [debug]: frame= 124 QP=29.43 NAL=0 Slice:B Poc:246 I:0 P:46 SKIP:350 size=87 bytes
x264 [debug]: frame= 125 QP=22.47 NAL=2 Slice:P Poc:256 I:0 P:106 SKIP:290 size=628 bytes
x264 [debug]: frame= 126 QP=28.03 NAL=2 Slice:B Poc:252 I:0 P:59 SKIP:337 size=114 bytes
x264 [debug]: frame= 127 QP=29.91 NAL=0 Slice:B Poc:250 I:0 P:29 SKIP:367 size=80 bytes
x264 [debug]: frame= 128 QP=30.10 NAL=0 Slice:B Poc:254 I:0 P:33 SKIP:363 size=54 bytes
x264 [debug]: frame= 129 QP=22.14 NAL=2 Slice:P Poc:264 I:0 P:137 SKIP:259 size=1008 bytes
x264 [debug]: frame= 130 QP=28.75 NAL=2 Slice:B Poc:260 I:0 P:67 SKIP:329 size=133 bytes
x264 [debug]: frame= 131 QP=29.45 NAL=0 Slice:B Poc:258 I:0 P:47 SKIP:349 size=80 bytes
x264 [debug]: frame= 132 QP=30.26 NAL=0 Slice:B Poc:262 I:0 P:62 SKIP:334 size=74 bytes
x264 [debug]: frame= 133 QP=22.53 NAL=2 Slice:P Poc:272 I:2 P:142 SKIP:252 size=1646 bytes
x264 [debug]: frame= 134 QP=28.71 NAL=2 Slice:B Poc:268 I:0 P:109 SKIP:287 size=234 bytes
x264 [debug]: frame= 135 QP=31.21 NAL=0 Slice:B Poc:266 I:0 P:68 SKIP:328 size=81 bytes
x264 [debug]: frame= 136 QP=30.86 NAL=0 Slice:B Poc:270 I:0 P:55 SKIP:341 size=133 bytes
x264 [debug]: frame= 137 QP=21.73 NAL=2 Slice:P Poc:280 I:3 P:115 SKIP:278 size=1559 bytes
x264 [debug]: frame= 138 QP=29.54 NAL=2 Slice:B Poc:276 I:0 P:75 SKIP:321 size=294 bytes
x264 [debug]: frame= 139 QP=30.35 NAL=0 Slice:B Poc:274 I:0 P:30 SKIP:366 size=140 bytes
x264 [debug]: frame= 140 QP=30.94 NAL=0 Slice:B Poc:278 I:0 P:53 SKIP:343 size=104 bytes
x264 [debug]: frame= 141 QP=21.67 NAL=2 Slice:P Poc:288 I:0 P:138 SKIP:258 size=1033 bytes
x264 [debug]: frame= 142 QP=28.68 NAL=2 Slice:B Poc:284 I:0 P:76 SKIP:320 size=114 bytes
x264 [debug]: frame= 143 QP=30.26 NAL=0 Slice:B Poc:282 I:0 P:53 SKIP:343 size=90 bytes
x264 [debug]: frame= 144 QP=28.00 NAL=0 Slice:B Poc:286 I:0 P:33 SKIP:363 size=52 bytes
x264 [debug]: frame= 145 QP=22.60 NAL=2 Slice:P Poc:296 I:0 P:125 SKIP:271 size=1013 bytes
x264 [debug]: frame= 146 QP=28.91 NAL=2 Slice:B Poc:292 I:0 P:62 SKIP:334 size=104 bytes
x264 [debug]: frame= 147 QP=30.55 NAL=0 Slice:B Poc:290 I:0 P:35 SKIP:361 size=62 bytes
x264 [debug]: frame= 148 QP=29.62 NAL=0 Slice:B Poc:294 I:0 P:45 SKIP:351 size=60 bytes
x264 [debug]: frame= 149 QP=21.91 NAL=2 Slice:P Poc:304 I:0 P:120 SKIP:276 size=1030 bytes
x264 [debug]: frame= 150 QP=29.21 NAL=2 Slice:B Poc:300 I:0 P:57 SKIP:339 size=159 bytes
x264 [debug]: frame= 151 QP=31.21 NAL=0 Slice:B Poc:298 I:0 P:33 SKIP:363 size=56 bytes
x264 [debug]: frame= 152 QP=29.44 NAL=0 Slice:B Poc:302 I:0 P:34 SKIP:362 size=82 bytes
x264 [debug]: frame= 153 QP=21.30 NAL=2 Slice:P Poc:308 I:0 P:114 SKIP:282 size=996 bytes
x264 [debug]: frame= 154 QP=30.35 NAL=0 Slice:B Poc:306 I:0 P:41 SKIP:355 size=101 bytes
x264 [debug]: frame= 155 QP=21.55 NAL=2 Slice:P Poc:316 I:0 P:138 SKIP:258 size=1715 bytes
x264 [debug]: frame= 156 QP=30.15 NAL=2 Slice:B Poc:312 I:0 P:73 SKIP:323 size=230 bytes
x264 [debug]: frame= 157 QP=30.35 NAL=0 Slice:B Poc:310 I:0 P:57 SKIP:339 size=114 bytes
x264 [debug]: frame= 158 QP=30.33 NAL=0 Slice:B Poc:314 I:0 P:63 SKIP:333 size=108 bytes
x264 [debug]: frame= 159 QP=20.76 NAL=2 Slice:P Poc:324 I:0 P:146 SKIP:250 size=1474 bytes
x264 [debug]: frame= 160 QP=29.82 NAL=2 Slice:B Poc:320 I:0 P:70 SKIP:326 size=154 bytes
x264 [debug]: frame= 161 QP=30.61 NAL=0 Slice:B Poc:318 I:0 P:58 SKIP:338 size=93 bytes
x264 [debug]: frame= 162 QP=30.61 NAL=0 Slice:B Poc:322 I:0 P:59 SKIP:337 size=80 bytes
x264 [debug]: frame= 163 QP=21.32 NAL=2 Slice:P Poc:332 I:0 P:145 SKIP:251 size=1094 bytes
x264 [debug]: frame= 164 QP=29.78 NAL=2 Slice:B Poc:328 I:0 P:77 SKIP:319 size=109 bytes
x264 [debug]: frame= 165 QP=28.00 NAL=0 Slice:B Poc:326 I:0 P:65 SKIP:331 size=70 bytes
x264 [debug]: frame= 166 QP=29.68 NAL=0 Slice:B Poc:330 I:0 P:28 SKIP:368 size=56 bytes
x264 [debug]: frame= 167 QP=21.01 NAL=2 Slice:P Poc:340 I:0 P:146 SKIP:250 size=1017 bytes
x264 [debug]: frame= 168 QP=25.40 NAL=2 Slice:B Poc:336 I:0 P:55 SKIP:341 size=91 bytes
x264 [debug]: frame= 169 QP=29.68 NAL=0 Slice:B Poc:334 I:0 P:38 SKIP:358 size=55 bytes
x264 [debug]: frame= 170 QP=28.00 NAL=0 Slice:B Poc:338 I:0 P:40 SKIP:356 size=46 bytes
x264 [debug]: frame= 171 QP=22.16 NAL=2 Slice:P Poc:348 I:0 P:76 SKIP:320 size=433 bytes
x264 [debug]: frame= 172 QP=27.00 NAL=2 Slice:B Poc:344 I:0 P:33 SKIP:363 size=48 bytes
x264 [debug]: frame= 173 QP=28.00 NAL=0 Slice:B Poc:342 I:0 P:20 SKIP:376 size=36 bytes
x264 [debug]: frame= 174 QP=28.00 NAL=0 Slice:B Poc:346 I:0 P:17 SKIP:379 size=31 bytes
x264 [debug]: frame= 175 QP=21.55 NAL=2 Slice:P Poc:356 I:0 P:118 SKIP:278 size=912 bytes
x264 [debug]: frame= 176 QP=28.68 NAL=2 Slice:B Poc:352 I:0 P:61 SKIP:335 size=112 bytes
x264 [debug]: frame= 177 QP=29.68 NAL=0 Slice:B Poc:350 I:0 P:40 SKIP:356 size=52 bytes
x264 [debug]: frame= 178 QP=30.10 NAL=0 Slice:B Poc:354 I:0 P:36 SKIP:360 size=61 bytes
x264 [debug]: frame= 179 QP=21.70 NAL=2 Slice:P Poc:364 I:2 P:123 SKIP:271 size=965 bytes
x264 [debug]: frame= 180 QP=29.22 NAL=2 Slice:B Poc:360 I:0 P:61 SKIP:335 size=173 bytes
x264 [debug]: frame= 181 QP=29.43 NAL=0 Slice:B Poc:358 I:0 P:36 SKIP:360 size=100 bytes
x264 [debug]: frame= 182 QP=29.68 NAL=0 Slice:B Poc:362 I:0 P:25 SKIP:371 size=51 bytes
x264 [debug]: frame= 183 QP=21.78 NAL=2 Slice:P Poc:372 I:0 P:90 SKIP:306 size=646 bytes
x264 [debug]: frame= 184 QP=27.94 NAL=2 Slice:B Poc:368 I:0 P:42 SKIP:354 size=76 bytes
x264 [debug]: frame= 185 QP=30.10 NAL=0 Slice:B Poc:366 I:0 P:33 SKIP:363 size=53 bytes
x264 [debug]: frame= 186 QP=28.00 NAL=0 Slice:B Poc:370 I:0 P:24 SKIP:372 size=42 bytes
x264 [debug]: frame= 187 QP=21.35 NAL=2 Slice:P Poc:380 I:0 P:110 SKIP:286 size=688 bytes
x264 [debug]: frame= 188 QP=28.46 NAL=2 Slice:B Poc:376 I:0 P:60 SKIP:336 size=195 bytes
x264 [debug]: frame= 189 QP=29.68 NAL=0 Slice:B Poc:374 I:0 P:28 SKIP:368 size=76 bytes
x264 [debug]: frame= 190 QP=30.37 NAL=0 Slice:B Poc:378 I:0 P:29 SKIP:367 size=81 bytes
x264 [debug]: frame= 191 QP=21.61 NAL=2 Slice:P Poc:388 I:0 P:88 SKIP:308 size=544 bytes
x264 [debug]: frame= 192 QP=28.43 NAL=2 Slice:B Poc:384 I:0 P:37 SKIP:359 size=72 bytes
x264 [debug]: frame= 193 QP=28.00 NAL=0 Slice:B Poc:382 I:0 P:23 SKIP:373 size=40 bytes
x264 [debug]: frame= 194 QP=28.00 NAL=0 Slice:B Poc:386 I:0 P:5 SKIP:391 size=21 bytes
x264 [debug]: frame= 195 QP=22.09 NAL=2 Slice:P Poc:396 I:0 P:114 SKIP:282 size=741 bytes
x264 [debug]: frame= 196 QP=28.78 NAL=2 Slice:B Poc:392 I:0 P:62 SKIP:334 size=95 bytes
x264 [debug]: frame= 197 QP=28.00 NAL=0 Slice:B Poc:390 I:0 P:34 SKIP:362 size=48 bytes
x264 [debug]: frame= 198 QP=28.00 NAL=0 Slice:B Poc:394 I:0 P:24 SKIP:372 size=42 bytes
x264 [debug]: frame= 199 QP=22.33 NAL=2 Slice:P Poc:404 I:0 P:133 SKIP:263 size=910 bytes
x264 [debug]: frame= 200 QP=30.21 NAL=2 Slice:B Poc:400 I:0 P:65 SKIP:331 size=93 bytes
x264 [debug]: frame= 201 QP=28.00 NAL=0 Slice:B Poc:398 I:0 P:60 SKIP:336 size=65 bytes
x264 [debug]: frame= 202 QP=28.00 NAL=0 Slice:B Poc:402 I:0 P:52 SKIP:344 size=57 bytes
x264 [debug]: frame= 203 QP=22.89 NAL=2 Slice:P Poc:412 I:0 P:97 SKIP:299 size=682 bytes
x264 [debug]: frame= 204 QP=29.09 NAL=2 Slice:B Poc:408 I:0 P:40 SKIP:356 size=92 bytes
x264 [debug]: frame= 205 QP=29.68 NAL=0 Slice:B Poc:406 I:0 P:32 SKIP:364 size=56 bytes
x264 [debug]: frame= 206 QP=28.00 NAL=0 Slice:B Poc:410 I:0 P:32 SKIP:364 size=47 bytes
x264 [debug]: frame= 207 QP=22.21 NAL=2 Slice:P Poc:420 I:1 P:107 SKIP:288 size=1187 bytes
x264 [debug]: frame= 208 QP=28.10 NAL=2 Slice:B Poc:416 I:0 P:64 SKIP:332 size=229 bytes
x264 [debug]: frame= 209 QP=29.96 NAL=0 Slice:B Poc:414 I:0 P:42 SKIP:354 size=108 bytes
x264 [debug]: frame= 210 QP=30.22 NAL=0 Slice:B Poc:418 I:0 P:40 SKIP:356 size=95 bytes
x264 [debug]: frame= 211 QP=22.05 NAL=2 Slice:P Poc:428 I:3 P:118 SKIP:275 size=1646 bytes
x264 [debug]: frame= 212 QP=29.56 NAL=2 Slice:B Poc:424 I:0 P:66 SKIP:330 size=323 bytes
x264 [debug]: frame= 213 QP=30.99 NAL=0 Slice:B Poc:422 I:0 P:43 SKIP:353 size=93 bytes
x264 [debug]: frame= 214 QP=30.80 NAL=0 Slice:B Poc:426 I:0 P:45 SKIP:351 size=107 bytes
x264 [debug]: frame= 215 QP=22.46 NAL=2 Slice:P Poc:436 I:2 P:145 SKIP:249 size=1726 bytes
x264 [debug]: frame= 216 QP=28.56 NAL=2 Slice:B Poc:432 I:0 P:94 SKIP:302 size=287 bytes
x264 [debug]: frame= 217 QP=30.35 NAL=0 Slice:B Poc:430 I:0 P:53 SKIP:343 size=138 bytes
x264 [debug]: frame= 218 QP=30.57 NAL=0 Slice:B Poc:434 I:0 P:51 SKIP:345 size=103 bytes
x264 [debug]: frame= 219 QP=21.98 NAL=2 Slice:P Poc:444 I:0 P:140 SKIP:256 size=1601 bytes
x264 [debug]: frame= 220 QP=29.42 NAL=2 Slice:B Poc:440 I:0 P:79 SKIP:317 size=219 bytes
x264 [debug]: frame= 221 QP=29.36 NAL=0 Slice:B Poc:438 I:0 P:49 SKIP:347 size=116 bytes
x264 [debug]: frame= 222 QP=30.55 NAL=0 Slice:B Poc:442 I:0 P:58 SKIP:338 size=94 bytes
x264 [debug]: frame= 223 QP=21.57 NAL=2 Slice:P Poc:452 I:0 P:136 SKIP:260 size=1538 bytes
x264 [debug]: frame= 224 QP=28.06 NAL=2 Slice:B Poc:448 I:0 P:65 SKIP:331 size=187 bytes
x264 [debug]: frame= 225 QP=32.02 NAL=0 Slice:B Poc:446 I:0 P:57 SKIP:339 size=94 bytes
x264 [debug]: frame= 226 QP=29.67 NAL=0 Slice:B Poc:450 I:0 P:37 SKIP:359 size=76 bytes
x264 [debug]: frame= 227 QP=21.71 NAL=2 Slice:P Poc:460 I:0 P:130 SKIP:266 size=882 bytes
x264 [debug]: frame= 228 QP=28.47 NAL=2 Slice:B Poc:456 I:0 P:56 SKIP:340 size=104 bytes
x264 [debug]: frame= 229 QP=28.00 NAL=0 Slice:B Poc:454 I:0 P:57 SKIP:339 size=73 bytes
x264 [debug]: frame= 230 QP=28.00 NAL=0 Slice:B Poc:458 I:0 P:38 SKIP:358 size=49 bytes
x264 [debug]: frame= 231 QP=21.78 NAL=2 Slice:P Poc:468 I:0 P:136 SKIP:260 size=969 bytes
x264 [debug]: frame= 232 QP=26.37 NAL=2 Slice:B Poc:464 I:0 P:76 SKIP:320 size=138 bytes
x264 [debug]: frame= 233 QP=28.00 NAL=0 Slice:B Poc:462 I:0 P:60 SKIP:336 size=65 bytes
x264 [debug]: frame= 234 QP=29.68 NAL=0 Slice:B Poc:466 I:0 P:38 SKIP:358 size=87 bytes
x264 [debug]: frame= 235 QP=21.87 NAL=2 Slice:P Poc:476 I:1 P:155 SKIP:240 size=1521 bytes
x264 [debug]: frame= 236 QP=28.76 NAL=2 Slice:B Poc:472 I:0 P:87 SKIP:309 size=202 bytes
x264 [debug]: frame= 237 QP=30.57 NAL=0 Slice:B Poc:470 I:0 P:71 SKIP:325 size=101 bytes
x264 [debug]: frame= 238 QP=30.45 NAL=0 Slice:B Poc:474 I:0 P:48 SKIP:348 size=97 bytes
x264 [debug]: frame= 239 QP=21.69 NAL=2 Slice:P Poc:484 I:0 P:132 SKIP:264 size=1135 bytes
x264 [debug]: frame= 240 QP=29.64 NAL=2 Slice:B Poc:480 I:0 P:82 SKIP:314 size=152 bytes
x264 [debug]: frame= 241 QP=28.62 NAL=0 Slice:B Poc:478 I:0 P:57 SKIP:339 size=83 bytes
x264 [debug]: frame= 242 QP=29.67 NAL=0 Slice:B Poc:482 I:0 P:63 SKIP:333 size=83 bytes
x264 [debug]: frame= 243 QP=21.72 NAL=2 Slice:P Poc:492 I:0 P:139 SKIP:257 size=1346 bytes
x264 [debug]: frame= 244 QP=28.80 NAL=2 Slice:B Poc:488 I:0 P:65 SKIP:331 size=173 bytes
x264 [debug]: frame= 245 QP=28.00 NAL=0 Slice:B Poc:486 I:0 P:35 SKIP:361 size=63 bytes
x264 [debug]: frame= 246 QP=29.41 NAL=0 Slice:B Poc:490 I:0 P:53 SKIP:343 size=89 bytes
x264 [debug]: frame= 247 QP=31.34 NAL=2 Slice:P Poc:498 I:0 P:57 SKIP:339 size=289 bytes
x264 [debug]: frame= 248 QP=30.08 NAL=2 Slice:B Poc:494 I:0 P:39 SKIP:357 size=92 bytes
x264 [debug]: frame= 249 QP=31.01 NAL=0 Slice:B Poc:496 I:0 P:44 SKIP:352 size=118 bytes
x264 [debug]: frame= 250 QP=16.74 NAL=3 Slice:I Poc:0 I:396 P:0 SKIP:0 size=15886 bytes
x264 [debug]: frame= 251 QP=21.51 NAL=2 Slice:P Poc:8 I:2 P:123 SKIP:271 size=1036 bytes
x264 [debug]: frame= 252 QP=28.92 NAL=2 Slice:B Poc:4 I:0 P:79 SKIP:317 size=166 bytes
x264 [debug]: frame= 253 QP=30.38 NAL=0 Slice:B Poc:2 I:0 P:41 SKIP:355 size=87 bytes
x264 [debug]: frame= 254 QP=30.27 NAL=0 Slice:B Poc:6 I:0 P:58 SKIP:338 size=79 bytes
x264 [debug]: frame= 255 QP=21.94 NAL=2 Slice:P Poc:16 I:0 P:131 SKIP:265 size=830 bytes
x264 [debug]: frame= 256 QP=27.98 NAL=2 Slice:B Poc:12 I:0 P:72 SKIP:324 size=107 bytes
x264 [debug]: frame= 257 QP=28.00 NAL=0 Slice:B Poc:10 I:0 P:44 SKIP:352 size=54 bytes
x264 [debug]: frame= 258 QP=29.09 NAL=0 Slice:B Poc:14 I:0 P:48 SKIP:348 size=65 bytes
x264 [debug]: frame= 259 QP=22.61 NAL=2 Slice:P Poc:24 I:4 P:138 SKIP:254 size=1466 bytes
x264 [debug]: frame= 260 QP=29.10 NAL=2 Slice:B Poc:20 I:0 P:74 SKIP:322 size=302 bytes
x264 [debug]: frame= 261 QP=30.66 NAL=0 Slice:B Poc:18 I:0 P:58 SKIP:338 size=117 bytes
x264 [debug]: frame= 262 QP=30.15 NAL=0 Slice:B Poc:22 I:0 P:56 SKIP:340 size=159 bytes
x264 [debug]: frame= 263 QP=22.99 NAL=2 Slice:P Poc:32 I:0 P:100 SKIP:296 size=782 bytes
x264 [debug]: frame= 264 QP=29.90 NAL=2 Slice:B Poc:28 I:0 P:69 SKIP:327 size=101 bytes
x264 [debug]: frame= 265 QP=27.47 NAL=0 Slice:B Poc:26 I:0 P:56 SKIP:340 size=70 bytes
x264 [debug]: frame= 266 QP=28.00 NAL=0 Slice:B Poc:30 I:0 P:35 SKIP:361 size=48 bytes
x264 [debug]: frame= 267 QP=22.99 NAL=2 Slice:P Poc:40 I:0 P:124 SKIP:272 size=698 bytes
x264 [debug]: frame= 268 QP=26.95 NAL=2 Slice:B Poc:36 I:0 P:70 SKIP:326 size=90 bytes
x264 [debug]: frame= 269 QP=28.00 NAL=0 Slice:B Poc:34 I:0 P:39 SKIP:357 size=54 bytes
x264 [debug]: frame= 270 QP=28.00 NAL=0 Slice:B Poc:38 I:0 P:42 SKIP:354 size=52 bytes
x264 [debug]: frame= 271 QP=23.44 NAL=2 Slice:P Poc:48 I:0 P:98 SKIP:298 size=686 bytes
x264 [debug]: frame= 272 QP=24.71 NAL=2 Slice:B Poc:44 I:0 P:57 SKIP:339 size=91 bytes
x264 [debug]: frame= 273 QP=28.00 NAL=0 Slice:B Poc:42 I:0 P:46 SKIP:350 size=52 bytes
x264 [debug]: frame= 274 QP=29.67 NAL=0 Slice:B Poc:46 I:0 P:35 SKIP:361 size=68 bytes
x264 [debug]: frame= 275 QP=24.08 NAL=2 Slice:P Poc:56 I:1 P:134 SKIP:261 size=1444 bytes
x264 [debug]: frame= 276 QP=29.15 NAL=2 Slice:B Poc:52 I:0 P:95 SKIP:301 size=247 bytes
x264 [debug]: frame= 277 QP=29.68 NAL=0 Slice:B Poc:50 I:0 P:56 SKIP:340 size=92 bytes
x264 [debug]: frame= 278 QP=31.68 NAL=0 Slice:B Poc:54 I:0 P:61 SKIP:335 size=127 bytes
x264 [debug]: frame= 279 QP=23.62 NAL=2 Slice:P Poc:64 I:0 P:138 SKIP:258 size=1447 bytes
x264 [debug]: frame= 280 QP=29.14 NAL=2 Slice:B Poc:60 I:0 P:89 SKIP:307 size=200 bytes
x264 [debug]: frame= 281 QP=31.50 NAL=0 Slice:B Poc:58 I:0 P:59 SKIP:337 size=123 bytes
x264 [debug]: frame= 282 QP=30.61 NAL=0 Slice:B Poc:62 I:0 P:63 SKIP:333 size=85 bytes
x264 [debug]: frame= 283 QP=23.93 NAL=2 Slice:P Poc:72 I:0 P:132 SKIP:264 size=1012 bytes
x264 [debug]: frame= 284 QP=29.30 NAL=2 Slice:B Poc:68 I:0 P:79 SKIP:317 size=165 bytes
x264 [debug]: frame= 285 QP=31.45 NAL=0 Slice:B Poc:66 I:0 P:61 SKIP:335 size=86 bytes
x264 [debug]: frame= 286 QP=30.34 NAL=0 Slice:B Poc:70 I:0 P:56 SKIP:340 size=90 bytes
x264 [debug]: frame= 287 QP=25.16 NAL=2 Slice:P Poc:80 I:0 P:106 SKIP:290 size=716 bytes
x264 [debug]: frame= 288 QP=29.13 NAL=2 Slice:B Poc:76 I:0 P:71 SKIP:325 size=122 bytes
x264 [debug]: frame= 289 QP=29.32 NAL=0 Slice:B Poc:74 I:0 P:49 SKIP:347 size=78 bytes
x264 [debug]: frame= 290 QP=28.00 NAL=0 Slice:B Poc:78 I:0 P:63 SKIP:333 size=77 bytes
x264 [debug]: frame= 291 QP=26.76 NAL=2 Slice:P Poc:88 I:0 P:90 SKIP:306 size=581 bytes
x264 [debug]: frame= 292 QP=29.47 NAL=2 Slice:B Poc:84 I:0 P:81 SKIP:315 size=190 bytes
x264 [debug]: frame= 293 QP=31.21 NAL=0 Slice:B Poc:82 I:0 P:47 SKIP:349 size=70 bytes
x264 [debug]: frame= 294 QP=28.00 NAL=0 Slice:B Poc:86 I:0 P:40 SKIP:356 size=67 bytes
x264 [debug]: frame= 295 QP=28.47 NAL=2 Slice:P Poc:96 I:0 P:71 SKIP:325 size=309 bytes
x264 [debug]: frame= 296 QP=28.67 NAL=2 Slice:B Poc:92 I:0 P:73 SKIP:323 size=219 bytes
x264 [debug]: frame= 297 QP=29.77 NAL=0 Slice:B Poc:90 I:0 P:58 SKIP:338 size=105 bytes
x264 [debug]: frame= 298 QP=29.61 NAL=0 Slice:B Poc:94 I:0 P:48 SKIP:348 size=79 bytes
x264 [debug]: frame= 299 QP=29.72 NAL=2 Slice:P Poc:98 I:0 P:19 SKIP:377 size=86 bytes

x264 [info]: frame I:2 Avg QP:18.16 size: 13905
x264 [info]: frame P:76 Avg QP:22.34 size: 1108
x264 [info]: frame B:222 Avg QP:29.15 size: 107
x264 [info]: consecutive B-frames: 1.0% 0.7% 1.0% 97.3%
x264 [info]: mb I I16..4: 6.6% 65.0% 28.4%
x264 [info]: mb P I16..4: 0.0% 0.1% 0.0% P16..4: 15.7% 9.9% 7.2% 0.0% 0.0% skip:67.0%
x264 [info]: mb B I16..4: 0.0% 0.0% 0.0% B16..8: 12.9% 1.1% 0.2% direct: 0.2% skip:85.7% L0:35.0% L1:57.7% BI: 7.3%
x264 [info]: 8x8 transform intra:65.0% inter:51.2%
x264 [info]: coded y,uvDC,uvAC intra: 91.8% 91.3% 77.2% inter: 3.1% 2.3% 0.4%
x264 [info]: i16 v,h,dc,p: 63% 12% 4% 21%
x264 [info]: i8 v,h,dc,ddl,ddr,vr,hd,vl,hu: 24% 27% 16% 4% 5% 7% 5% 6% 6%
x264 [info]: i4 v,h,dc,ddl,ddr,vr,hd,vl,hu: 31% 10% 10% 6% 7% 12% 6% 12% 6%
x264 [info]: i8c dc,h,v,p: 40% 24% 27% 9%
x264 [info]: Weighted P-Frames: Y:0.0% UV:0.0%
x264 [info]: ref P L0: 62.2% 16.1% 14.3% 7.5%
x264 [info]: ref B L0: 91.8% 6.2% 2.0%
x264 [info]: ref B L1: 95.9% 4.1%
x264 [info]: kb/s:108.45

encoded 300 frames, 1362.52 fps, 108.45 kb/s
mirafra@mirafra:~/x264$
------------------------------------------------------------------------------------------------------------------------
./x264: Invokes the x264 encoder executable.
--log-level debug: Sets the logging level to debug, providing detailed frame-by-frame information (e.g., QP, NAL unit type, slice type, macroblock details).
--preset medium: Uses the medium preset, which balances encoding speed and compression efficiency. Presets range from ultrafast (fastest, least compression) to veryslow (slowest, best compression).
--crf 23: Specifies Constant Rate Factor (CRF) mode with a value of 23. CRF is a quality-based encoding mode where lower values (e.g., 18) produce higher quality and larger files, and higher values (e.g., 28) produce lower quality and smaller files. CRF 23 is a common choice for good quality with reasonable file sizes.
--output output.h264: Specifies the output file (output.h264), which will contain the encoded H.264 video stream.
input.y4m: The input file in YUV4MPEG2 format, a raw video format commonly used for encoding.

### Log Output Analysis
#### Input Video Information
text
Copy
y4m [info]: 352x288p 128:117 @ 30000/1001 fps (cfr)
- Resolution: 352x288 pixels (CIF resolution, common for older or low-resolution video).
- Aspect Ratio: Sample Aspect Ratio (SAR) of 128:117, meaning the pixels are not square, and the display aspect ratio (DAR) is adjusted accordingly.
- Frame Rate: 30000/1001 ≈ 29.97 fps (NTSC standard, constant frame rate or CFR).
#### Encoder Settings
text
Copy
x264 [debug]: using mv_range_thread = 24 x264 [info]: using SAR=128/117 x264 [info]: using cpu capabilities: MMX2 SSE2Fast SSSE3 SSE4.2 AVX FMA3 BMI2 AVX2 AVX512 x264 [info]: profile High, level 1.3, 4:2:0, 8-bit
- mv_range_thread = 24: Limits the motion vector search range for multi-threaded encoding, optimizing performance.
- SAR=128/117: Confirms the aspect ratio from the input.
- CPU Capabilities: Lists the CPU instruction sets used (e.g., AVX, AVX2, AVX512), indicating that x264 is leveraging advanced CPU features for faster encoding.
- Profile and Level:
  - High Profile: Supports advanced features like 8x8 DCT, custom quantization matrices, and more, suitable for high-quality encoding.
  - Level 1.3: Restricts parameters (e.g., max bitrate, frame size) to ensure compatibility with low-end devices. For 352x288 at 29.97 fps, Level 1.3 is sufficient.
  - 4:2:0, 8-bit: Uses 4:2:0 chroma subsampling (common for consumer video) and 8-bit color depth.
#### Frame-by-Frame Debug Output
The debug log provides detailed statistics for each frame (e.g., frame 0 to 299). Here’s an example for frame 0:
text
Copy
x264 [debug]: frame= 0 QP=19.57 NAL=3 Slice:I Poc:0 I:396 P:0 SKIP:0 size=11924 bytes
- Frame Number: 0 (first frame).
- QP (Quantization Parameter): 19.57. Lower QP values indicate higher quality (less compression); 19.57 is relatively low, suggesting good quality for this I-frame.
- NAL (Network Abstraction Layer) Unit: Type 3 (likely an IDR frame, a type of I-frame that serves as a keyframe for random access).
- Slice Type: I (Intra-coded frame, encoded without reference to other frames).
- Poc (Picture Order Count): 0 (display order position).
- Macroblocks:
  - I:396: All 396 macroblocks (352x288 ÷ 16x16 = 396) are intra-coded.
  - P:0, SKIP:0: No predicted or skipped macroblocks, as expected for an I-frame.
- Size: 11924 bytes (relatively large, typical for I-frames due to full intra-coding).
For P-frames (e.g., frame 1):
text
Copy
x264 [debug]: frame= 1 QP=20.79 NAL=2 Slice:P Poc:8 I:0 P:93 SKIP:303 size=485 bytes
- Slice Type: P (Predictive frame, uses motion compensation from previous frames).
- P:93, SKIP:303: 93 macroblocks are predicted, and 303 are skipped (no changes from the reference frame, reducing data).
- Size: 485 bytes (much smaller than I-frames due to prediction and skipping).
For B-frames (e.g., frame 2):
text
Copy
x264 [debug]: frame= 2 QP=27.00 NAL=2 Slice:B Poc:4 I:0 P:47 SKIP:349 size=52 bytes
- Slice Type: B (Bi-predictive frame, uses references from both past and future frames).
- QP=27.00: Higher QP (more compression, lower quality) than I- or P-frames, as B-frames are less critical.
- Size: 52 bytes (very small, due to high skip rate and bi-prediction efficiency).
#### Summary Statistics
text
Copy
x264 [info]: frame I:2 Avg QP:18.16 size: 13905 x264 [info]: frame P:76 Avg QP:22.34 size: 1108 x264 [info]: frame B:222 Avg QP:29.15 size: 107 x264 [info]: consecutive B-frames: 1.0% 0.7% 1.0% 97.3%
- Frame Counts:
  - I-frames: 2 (keyframes, large size: ~13.9 KB average).
  - P-frames: 76 (predictive frames, ~1.1 KB average).
  - B-frames: 222 (bi-predictive frames, ~107 bytes average).
- Average QP:
  - I-frames: 18.16 (high quality).
  - P-frames: 22.34 (good quality).
  - B-frames: 29.15 (lower quality, more compression).
- B-frame Usage: 97.3% of frames have 3 consecutive B-frames, indicating heavy use of B-frames for compression efficiency (typical for the medium preset).
text
Copy
x264 [info]: mb I I16..4: 6.6% 65.0% 28.4% x264 [info]: mb P I16..4: 0.0% 0.1% 0.0% P16..4: 15.7% 9.9% 7.2% 0.0% 0.0% skip:67.0% x264 [info]: mb B I16..4: 0.0% 0.0% 0.0% B16..8: 12.9% 1.1% 0.2% direct: 0.2% skip:85.7%
- Macroblock Types:
  - I-frames: Mostly use 16x16 (65%) and 4x4 (28.4%) intra prediction.
  - P-frames: 67% of macroblocks are skipped, with 15.7% using 16x16 prediction.
  - B-frames: 85.7% are skipped, with 12.9% using 16x16 bi-prediction.
text
Copy
x264 [info]: 8x8 transform intra:65.0% inter:51.2% x264 [info]: coded y,uvDC,uvAC intra: 91.8% 91.3% 77.2% inter: 3.1% 2.3% 0.4%
- 8x8 Transform: Used for 65% of intra blocks and 51.2% of inter blocks, improving compression for high-profile encoding.
- Coded Components: High percentage of luma (Y) and chroma (UV) coefficients are coded for intra frames, while inter frames have minimal coding (due to skipping).
text
Copy
x264 [info]: kb/s:108.45 encoded 300 frames, 1362.52 fps, 108.45 kb/s
- Bitrate: 108.45 kbps (low, due to small resolution and CRF 23).
- Frame Count: 300 frames encoded.
- Encoding Speed: 1362.52 fps (very fast, likely due to small resolution and hardware acceleration).
- Output Bitrate: 108.45 kbps, suitable for low-bandwidth applications.

------------------------------------------------------------------------------------------------------------------------
This file provides a detailed breakdown of CPU cycle samples collected during the x264 encoding process, with 5,212 samples and an approximate event count of 3,104,072,026 cycles. The goal is to determine which x264 module—Intra Prediction, Transform, Entropy Coding, or Motion Estimation—consumed the most CPU cycles and rank them accordingly.
Below, I’ll analyze the perf_report.txt data, map the listed functions to the four modules, aggregate their cycle usage, and provide a ranking. I’ll also estimate the absolute cycle counts, address the kernel symbol restriction warning, and suggest optimizations for the most cycle-intensive module. The analysis is based on the provided data, your previous x264 log (300 frames, 352x288, medium preset, CRF 23, High Profile with CABAC), and general knowledge of x264’s architecture.

### Step 1: Mapping Functions to Modules
To identify the cycle-intensive modules, I’ll map the functions in perf_report.txt to the four modules: Intra Prediction, Transform, Entropy Coding, and Motion Estimation. I’ll focus on functions with significant overhead (e.g., >0.5%) and cross-reference with x264’s source code to categorize them. Below are the key functions for each module, followed by the analysis of the report.
#### Module Function Mappings
- Intra Prediction:
  - Functions related to intra mode decision and prediction.
  - Examples: x264_8_mb_analyse_intra, x264_8_intra_satd_x9_4x4_avx, x264_8_intra_satd_x3_8x8c_ssse3, x264_8_intra_satd_x3_16x16_ssse3, x264_8_intra_sa8d_x9_8x8_avx.
  - Computes SATD (Sum of Absolute Transformed Differences) for intra modes.
- Transform:
  - Functions for DCT (Discrete Cosine Transform), quantization, and inverse transforms.
  - Examples: x264_8_dct4x4x4_internal_avx512, x264_8_quant_4x4x4_avx2, x264_8_quant_4x4_avx2, x264_8_quant_8x8_avx2, x264_8_sub16x16_dct_avx512, x264_8_sub16x16_dct8_avx2, x264_8_sub8x8_dct_avx512, x264_8_sub8x8_dct_dc_avx512, x264_8_add8x8_idct_avx512.
  - Includes Hadamard transforms: x264_8_hadamard_ac_8x8_avx2, x264_8_pixel_hadamard_ac_16x16_avx2.
- Entropy Coding:
  - Functions for CABAC (Context-Adaptive Binary Arithmetic Coding) encoding.
  - Examples: x264_8_cabac_block_residual_rd_internal_avx512, x264_8_cabac_block_residual_8x8_rd_internal_avx512, x264_8_cabac_encode_decision_asm, x264_8_cabac_encode_decision_bmi2, x264_8_trellis_cabac_4x4_ssse3, x264_8_trellis_cabac_8x8_ssse3, x264_8_macroblock_write_cabac, cabac_mvd, cabac_cbp_luma, cabac_qp_delta.
  - Includes trellis quantization: x264_8_quant_4x4_trellis, x264_8_trellis_coef1, x264_8_trellis_coefn, x264_8_trellis_bnode_0, trellis_dc_shortcut.
- Motion Estimation:
  - Functions for motion vector search, subpixel refinement, and inter prediction.
  - Examples: x264_8_me_search_ref, get_ref_avx2, refine_subpel, x264_8_pixel_satd_8x8_internal_avx512, x264_8_pixel_sad_x4_16x16_avx512, x264_8_mc_chroma_avx2, x264_8_pixel_satd_16x8_internal_avx512, x264_8_pixel_satd_8x8_avx512, x264_8_pixel_avg2_w16_sse2, x264_8_pixel_sad_x3_16x16_avx512, x264_8_pixel_avg2_w8_mmx2, x264_8_mb_predict_mv_ref16x16, x264_8_pixel_sad_16x16_avx512, x264_8_mb_encode_chroma, x264_8_hpel_filter_avx2, x264_8_pixel_sad_x4_8x8_avx512, x264_8_mb_predict_mv, x264_8_pixel_ssd_16x16_avx2, x264_8_pixel_sad_x3_8x8_avx512, x264_8_pixel_satd_4x4_avx512, x264_8_pixel_ssd_8x8_avx, mb_mc_01xywh, x264_8_mb_predict_mv_direct16x16, x264_8_pixel_var2_8x8_avx512, x264_8_pixel_var_16x16_avx512, mb_analyse_inter_b8x8_mixed_ref, mb_analyse_inter_b16x16, mb_analyse_inter_direct, mb_analyse_inter_p8x8_mixed_ref, mb_analyse_inter_p16x16, x264_8_mb_mc, mc_luma_sse2, x264_8_prefetch_fenc_420_mmx2, mb_load_mv_direct8x8, x264_8_pixel_avg_weight_w8_avx512, x264_8_mc_offsetsub_w8_mmx2, x264_8_mc_offsetsub_w16_sse2.
  - Includes SAD (Sum of Absolute Differences) and SSD (Sum of Squared Differences) calculations.
#### Notes on Function Mapping
- Many functions are optimized with SIMD instructions (e.g., AVX2, AVX512, SSE2), as seen in suffixes like _avx512, _avx2, _sse2. These are still part of the respective modules.
- Some functions (e.g., rd_cost_mb, slicetype_mb_cost, x264_8_macroblock_analyse) involve multiple modules. I’ll allocate their contributions based on their primary role or split them proportionally.
- Functions like x264_8_macroblock_cache_load_progressive, x264_8_macroblock_cache_save, and x264_8_mbtree_propagate_list_internal_avx512 are auxiliary (cache management, MB-tree propagation). I’ll exclude them from module-specific counts unless they clearly belong to a module.

### Step 2: Analyzing perf_report.txt
I’ll extract the top functions (overhead >0.5%) from perf_report.txt, categorize them into modules, and sum their overhead percentages. Functions not directly related to the four modules (e.g., kernel functions, libpthread, libc) or with ambiguous roles will be noted separately.
#### Top Functions (Overhead >0.5%)
Here’s the list of functions with overhead >0.5%, along with their module assignments:
1. 10.38% - [unknown] [k] 0000000000000000 (includes rd_cost_mb (0.66%), x264_8_plane_copy_avx512 (0.60%), x264_8_macroblock_cache_save (0.51%)):
  1. rd_cost_mb: Rate-distortion cost calculation (involves Motion Estimation and Transform).
  2. x264_8_plane_copy_avx512: Memory copy (auxiliary, not module-specific).
  3. x264_8_macroblock_cache_save: Cache management (auxiliary).
  4. Assignment: Split rd_cost_mb (0.66%) between Motion Estimation (0.33%) and Transform (0.33%). Exclude others.
2. 4.90% - x264_8_me_search_ref:
  1. Motion vector search.
  2. Assignment: Motion Estimation.
3. 4.75% - get_ref_avx2:
  1. Reference frame access for motion estimation.
  2. Assignment: Motion Estimation.
4. 4.34% - refine_subpel:
  1. Subpixel motion refinement.
  2. Assignment: Motion Estimation.
5. 3.70% - x264_8_pixel_satd_8x8_internal_avx512:
  1. SATD calculation for motion estimation.
  2. Assignment: Motion Estimation.
6. 3.69% - x264_8_pixel_sad_x4_16x16_avx512:
  1. SAD calculation for motion estimation.
  2. Assignment: Motion Estimation.
7. 3.66% - x264_8_mc_chroma_avx2:
  1. Chroma motion compensation.
  2. Assignment: Motion Estimation.
8. 3.42% - x264_8_pixel_satd_16x8_internal_avx512:
  1. SATD calculation for motion estimation.
  2. Assignment: Motion Estimation.
9. 3.39% - [unknown] [k] 0x0000000000000001 (includes x264_8_mbtree_propagate_list_internal_avx512 (1.09%), cabac_mvd (0.72%)):
  1. x264_8_mbtree_propagate_list_internal_avx512: MB-tree propagation (auxiliary).
  2. cabac_mvd: CABAC encoding of motion vector differences.
  3. Assignment: cabac_mvd (0.72%) to Entropy Coding. Exclude MB-tree.
10. 3.26% - x264_8_pixel_satd_8x8_avx512:
  1. SATD calculation for motion estimation.
  2. Assignment: Motion Estimation.
11. 2.99% - x264_8_pixel_avg2_w16_sse2:
  1. Pixel averaging for motion compensation.
  2. Assignment: Motion Estimation.
12. 2.52% - [unknown] [.] 0xffffffff82600124:
  1. Kernel-related (not module-specific).
  2. Assignment: Exclude.
13. 2.33% - [unknown] [.] 0xffffffff8258d894:
  1. Kernel-related.
  2. Assignment: Exclude.
14. 2.23% - rd_cost_mb:
  1. Rate-distortion cost (Motion Estimation and Transform).
  2. Assignment: Split between Motion Estimation (1.12%) and Transform (1.11%).
15. 1.91% - x264_8_hadamard_ac_8x8_avx2:
  1. Hadamard transform for transform module.
  2. Assignment: Transform.
16. 1.78% - __pthread_mutex_lock (libpthread):
  1. Thread synchronization (not module-specific).
  2. Assignment: Exclude.
17. 1.74% - slicetype_mb_cost:
  1. Slice type decision (involves Motion Estimation and Intra Prediction).
  2. Assignment: Split between Motion Estimation (0.87%) and Intra Prediction (0.87%).
18. 1.70% - x264_8_pixel_sad_x3_16x16_avx512:
  1. SAD calculation for motion estimation.
  2. Assignment: Motion Estimation.
19. 1.60% - x264_8_pixel_avg2_w8_mmx2:
  1. Pixel averaging for motion compensation.
  2. Assignment: Motion Estimation.
20. 1.48% - [unknown] [k] 0x0000000200000120 (includes x264_8_pixel_ssd_8x8_avx (0.81%)):
  1. SSD calculation for motion estimation.
  2. Assignment: Motion Estimation (0.81%).
21. 1.48% - x264_8_macroblock_cache_load_progressive:
  1. Cache management (auxiliary).
  2. Assignment: Exclude.
22. 1.44% - x264_8_macroblock_encode:
  1. General macroblock encoding (involves Transform and Entropy Coding).
  2. Assignment: Split between Transform (0.72%) and Entropy Coding (0.72%).
23. 1.43% - [unknown] [.] 0xffffffff81803602:
  1. Kernel-related.
  2. Assignment: Exclude.
24. 1.43% - [unknown] [.] 0xffffffff81993e1b:
  1. Kernel-related.
  2. Assignment: Exclude.
25. 1.39% - analyse_update_cache:
  1. Cache update (auxiliary).
  2. Assignment: Exclude.
26. 1.27% - x264_8_mb_predict_mv_ref16x16:
  1. Motion vector prediction.
  2. Assignment: Motion Estimation.
27. 1.26% - x264_8_pixel_sad_16x16_avx512:
  1. SAD calculation for motion estimation.
  2. Assignment: Motion Estimation.
28. 1.22% - x264_8_mb_encode_chroma:
  1. Chroma encoding (Motion Estimation and Transform).
  2. Assignment: Motion Estimation (0.61%), Transform (0.61%).
29. 1.20% - x264_8_quant_4x4x4_avx2:
  1. Quantization.
  2. Assignment: Transform.
30. 1.16% - x264_8_hpel_filter_avx2:
  1. Half-pixel filtering for motion estimation.
  2. Assignment: Motion Estimation.
31. 1.14% - x264_8_pixel_sad_x4_8x8_avx512:
  1. SAD calculation for motion estimation.
  2. Assignment: Motion Estimation.
32. 1.13% - __pthread_mutex_unlock (libpthread):
  1. Thread synchronization.
  2. Assignment: Exclude.
33. 1.10% - x264_8_mb_predict_mv:
  1. Motion vector prediction.
  2. Assignment: Motion Estimation.
34. 1.09% - x264_8_mbtree_propagate_list_internal_avx512:
  1. MB-tree propagation (auxiliary).
  2. Assignment: Exclude.
35. 1.08% - x264_8_pixel_ssd_16x16_avx2:
  1. SSD calculation for motion estimation.
  2. Assignment: Motion Estimation.
36. 1.06% - x264_8_pixel_sad_x3_8x8_avx512:
  1. SAD calculation for motion estimation.
  2. Assignment: Motion Estimation.
37. 1.05% - [unknown] [.] 0xffffffff82600c07:
  1. Kernel-related.
  2. Assignment: Exclude.
38. 0.96% - [unknown] [.] 0xffffffff82591e57:
  1. Kernel-related.
  2. Assignment: Exclude.
39. 0.93% - [unknown] [.] 0xffffffff818a2ba2:
  1. Kernel-related.
  2. Assignment: Exclude.
40. 0.91% - x264_8_frame_expand_border_filtered:
  1. Frame border expansion (auxiliary).
  2. Assignment: Exclude.
41. 0.90% - x264_8_dct4x4x4_internal_avx512:
  1. DCT transform.
  2. Assignment: Transform.
42. 0.90% - x264_8_cabac_block_residual_rd_internal_avx512:
  1. CABAC residual encoding.
  2. Assignment: Entropy Coding.
43. 0.87% - [unknown] [.] 0xffffffff81b02328:
  1. Kernel-related.
  2. Assignment: Exclude.
44. 0.87% - [unknown] [.] 0xffffffff8199335a:
  1. Kernel-related.
  2. Assignment: Exclude.
45. 0.86% - x264_8_pixel_satd_4x4_avx512:
  1. SATD calculation for motion estimation.
  2. Assignment: Motion Estimation.
46. 0.85% - cabac_mvd:
  1. CABAC motion vector encoding.
  2. Assignment: Entropy Coding.
47. 0.81% - x264_8_pixel_ssd_8x8_avx:
  1. SSD calculation for motion estimation.
  2. Assignment: Motion Estimation.
48. 0.80% - mb_mc_01xywh:
  1. Motion compensation.
  2. Assignment: Motion Estimation.
49. 0.79% - [unknown] [.] 0xffffffff8259c1d9:
  1. Kernel-related.
  2. Assignment: Exclude.
50. 0.79% - pthread_cond_wait@@GLIBC_2.3.2 (libpthread):
  1. Thread synchronization.
  2. Assignment: Exclude.
51. 0.78% - x264_8_frame_init_lowres_core_avx2:
  1. Low-resolution frame initialization (auxiliary).
  2. Assignment: Exclude.
52. 0.73% - [unknown] [.] 0xffffffff819914f5:
  1. Kernel-related.
  2. Assignment: Exclude.
53. 0.73% - [unknown] [.] 0xffffffff81990648:
  1. Kernel-related.
  2. Assignment: Exclude.
54. 0.70% - x264_8_mb_predict_mv_direct16x16:
  1. Motion vector prediction for direct mode.
  2. Assignment: Motion Estimation.
55. 0.70% - x264_8_trellis_cabac_4x4_ssse3:
  1. Trellis-based CABAC encoding.
  2. Assignment: Entropy Coding.
56. 0.68% - x264_8_macroblock_analyse:
  1. Macroblock analysis (involves Motion Estimation and Intra Prediction).
  2. Assignment: Split between Motion Estimation (0.34%) and Intra Prediction (0.34%).
57. 0.64% - x264_8_trellis_cabac_8x8_ssse3:
  1. Trellis-based CABAC encoding.
  2. Assignment: Entropy Coding.
58. 0.62% - x264_8_pixel_sad_8x8_avx512:
  1. SAD calculation for motion estimation.
  2. Assignment: Motion Estimation.
59. 0.61% - x264_8_plane_copy_interleave_core_sse2:
  1. Memory copy (auxiliary).
  2. Assignment: Exclude.
60. 0.60% - x264_8_plane_copy_avx512:
  1. Memory copy (auxiliary).
  2. Assignment: Exclude.
61. 0.59% - cabac_cbp_luma:
  1. CABAC encoding of luma CBP.
  2. Assignment: Entropy Coding.
62. 0.59% - __memmove_avx_unaligned_erms (libc):
  1. Memory copy (auxiliary).
  2. Assignment: Exclude.
63. 0.58% - __munmap (libc):
  1. Memory management (auxiliary).
  2. Assignment: Exclude.
64. 0.56% - x264_8_macroblock_cache_save:
  1. Cache management (auxiliary).
  2. Assignment: Exclude.
65. 0.56% - [unknown] [.] 0xffffffff819932fb:
  1. Kernel-related.
  2. Assignment: Exclude.
66. 0.56% - [unknown] [.] 0xffffffff818043e7:
  1. Kernel-related.
  2. Assignment: Exclude.
67. 0.56% - [unknown] [.] 0xffffffff81b0915d:
  1. Kernel-related.
  2. Assignment: Exclude.
68. 0.56% - [unknown] [.] 0xffffffff81b09059:
  1. Kernel-related.
  2. Assignment: Exclude.
69. 0.55% - x264_8_hadamard_load:
  1. Hadamard transform loading (Transform).
  2. Assignment: Transform.
70. 0.55% - x264_8_memcpy_aligned_avx512:
  1. Memory copy (auxiliary).
  2. Assignment: Exclude.
71. 0.55% - [unknown] [.] 0xffffffffff0bff08:
  1. Unknown (likely kernel).
  2. Assignment: Exclude.
72. 0.55% - [unknown] [.] 0xffffffff81b02214:
  1. Kernel-related.
  2. Assignment: Exclude.
73. 0.54% - mb_analyse_inter_b8x8_mixed_ref:
  1. Inter prediction analysis for B-frames.
  2. Assignment: Motion Estimation.
74. 0.51% - mb_analyse_inter_b16x16:
  1. Inter prediction analysis for B-frames.
  2. Assignment: Motion Estimation.
75. 0.51% - [unknown] [.] 0xffffffff81b08cba:
  1. Kernel-related.
  2. Assignment: Exclude.
#### Lower-Overhead Functions (0.1% to 0.5%)
To ensure completeness, I’ll include relevant functions with lower overhead that clearly belong to a module:
- Intra Prediction:
  - x264_8_intra_satd_x9_4x4_avx (0.26%)
  - x264_8_intra_satd_x3_8x8c_ssse3 (0.23%)
  - x264_8_intra_sa8d_x9_8x8_avx (0.20%)
  - x264_8_intra_satd_x3_16x16_ssse3 (0.16%)
  - mb_analyse_intra (0.16%)
- Transform:
  - x264_8_quant_8x8_avx2 (0.23%)
  - x264_8_sub16x16_dct_avx512 (0.28%)
  - x264_8_sub16x16_dct8_avx2 (0.22%)
  - x264_8_sub8x8_dct_avx512 (0.12%)
  - x264_8_sub8x8_dct_dc_avx512 (0.13%)
  - x264_8_add8x8_idct_avx512 (0.15%)
  - x264_8_quant_4x4_avx2 (0.14%)
  - x264_8_quant_2x2_dc_ssse3 (0.12%)
- Entropy Coding:
  - x264_8_cabac_block_residual_8x8_rd_internal_avx512 (0.27%)
  - x264_8_cabac_encode_decision_asm (0.35%)
  - x264_8_cabac_encode_decision_bmi2 (0.30%)
  - x264_8_quant_4x4_trellis (0.26%)
  - x264_8_macroblock_write_cabac (0.21%)
  - x264_8_trellis_coef1 (0.20%)
  - x264_8_trellis_coefn (0.14%)
  - x264_8_trellis_bnode_0 (0.12%)
  - trellis_dc_shortcut (0.12%)
- Motion Estimation:
  - x264_8_pixel_satd_16x16_avx512 (0.25%)
  - x264_8_pixel_sad_x4_8x16_avx512 (0.23%)
  - x264_8_mb_mc (0.26%)
  - mc_luma_sse2 (0.24%)
  - x264_8_prefetch_fenc_420_mmx2 (0.22%)
  - x264_8_pixel_avg_weight_w8_avx512 (0.18%)
  - x264_8_mc_offsetsub_w8_mmx2 (0.17%)
  - x264_8_mc_offsetsub_w16_sse2 (0.17%)
  - x264_8_pixel_satd_4x8_avx512 (0.12%)
  - x264_8_pixel_sad_8x16_avx512 (0.14%)
  - mb_analyse_inter_direct (0.37%)
  - mb_analyse_inter_p8x8_mixed_ref (0.34%)
  - mb_analyse_inter_p16x16 (0.16%)
  - mb_load_mv_direct8x8 (0.19%)
  - x264_8_mb_predict_mv_16x16 (0.30%)
  - mb_mc_0xywh (0.30%)

### Step 3: Aggregating Cycle Usage by Module
I’ll sum the overhead percentages for each module, including both high-overhead (>0.5%) and relevant lower-overhead (0.1% to 0.5%) functions. For functions that span multiple modules (e.g., rd_cost_mb), I’ve split their contributions as noted.
#### Intra Prediction
- slicetype_mb_cost (0.87%, split from 1.74%)
- x264_8_macroblock_analyse (0.34%, split from 0.68%)
- x264_8_intra_satd_x9_4x4_avx (0.26%)
- x264_8_intra_satd_x3_8x8c_ssse3 (0.23%)
- x264_8_intra_sa8d_x9_8x8_avx (0.20%)
- x264_8_intra_satd_x3_16x16_ssse3 (0.16%)
- mb_analyse_intra (0.16%)
- Total: 0.87 + 0.34 + 0.26 + 0.23 + 0.20 + 0.16 + 0.16 = 2.22%
#### Transform
- rd_cost_mb (0.33%, split from 0.66%)
- rd_cost_mb (1.11%, split from 2.23%)
- x264_8_hadamard_ac_8x8_avx2 (1.91%)
- x264_8_macroblock_encode (0.72%, split from 1.44%)
- x264_8_mb_encode_chroma (0.61%, split from 1.22%)
- x264_8_quant_4x4x4_avx2 (1.20%)
- x264_8_dct4x4x4_internal_avx512 (0.90%)
- x264_8_hadamard_load (0.55%)
- x264_8_quant_8x8_avx2 (0.23%)
- x264_8_sub16x16_dct_avx512 (0.28%)
- x264_8_sub16x16_dct8_avx2 (0.22%)
- x264_8_sub8x8_dct_avx512 (0.12%)
- x264_8_sub8x8_dct_dc_avx512 (0.13%)
- x264_8_add8x8_idct_avx512 (0.15%)
- x264_8_quant_4x4_avx2 (0.14%)
- x264_8_quant_2x2_dc_ssse3 (0.12%)
- Total: 0.33 + 1.11 + 1.91 + 0.72 + 0.61 + 1.20 + 0.90 + 0.55 + 0.23 + 0.28 + 0.22 + 0.12 + 0.13 + 0.15 + 0.14 + 0.12 = 8.62%
#### Entropy Coding
- cabac_mvd (0.72%, from [unknown] [k] 0x0000000000000001)
- x264_8_macroblock_encode (0.72%, split from 1.44%)
- x264_8_cabac_block_residual_rd_internal_avx512 (0.90%)
- cabac_mvd (0.85%)
- x264_8_trellis_cabac_4x4_ssse3 (0.70%)
- x264_8_trellis_cabac_8x8_ssse3 (0.64%)
- cabac_cbp_luma (0.59%)
- x264_8_cabac_block_residual_8x8_rd_internal_avx512 (0.27%)
- x264_8_cabac_encode_decision_asm (0.35%)
- x264_8_cabac_encode_decision_bmi2 (0.30%)
- x264_8_quant_4x4_trellis (0.26%)
- x264_8_macroblock_write_cabac (0.21%)
- x264_8_trellis_coef1 (0.20%)
- x264_8_trellis_coefn (0.14%)
- x264_8_trellis_bnode_0 (0.12%)
- trellis_dc_shortcut (0.12%)
- cabac_qp_delta (0.17%)
- Total: 0.72 + 0.72 + 0.90 + 0.85 + 0.70 + 0.64 + 0.59 + 0.27 + 0.35 + 0.30 + 0.26 + 0.21 + 0.20 + 0.14 + 0.12 + 0.12 + 0.17 = 6.76%
#### Motion Estimation
- rd_cost_mb (0.33%, split from 0.66%)
- x264_8_me_search_ref (4.90%)
- get_ref_avx2 (4.75%)
- refine_subpel (4.34%)
- x264_8_pixel_satd_8x8_internal_avx512 (3.70%)
- x264_8_pixel_sad_x4_16x16_avx512 (3.69%)
- x264_8_mc_chroma_avx2 (3.66%)
- x264_8_pixel_satd_16x8_internal_avx512 (3.42%)
- x264_8_pixel_satd_8x8_avx512 (3.26%)
- x264_8_pixel_avg2_w16_sse2 (2.99%)
- rd_cost_mb (1.12%, split from 2.23%)
- slicetype_mb_cost (0.87%, split from 1.74%)
- x264_8_pixel_sad_x3_16x16_avx512 (1.70%)
- x264_8_pixel_avg2_w8_mmx2 (1.60%)
- x264_8_pixel_ssd_8x8_avx (0.81%, from [unknown] [k] 0x0000000200000120)
- x264_8_macroblock_analyse (0.34%, split from 0.68%)
- x264_8_mb_predict_mv_ref16x16 (1.27%)
- x264_8_pixel_sad_16x16_avx512 (1.26%)
- x264_8_mb_encode_chroma (0.61%, split from 1.22%)
- x264_8_hpel_filter_avx2 (1.16%)
- x264_8_pixel_sad_x4_8x8_avx512 (1.14%)
- x264_8_mb_predict_mv (1.10%)
- x264_8_pixel_ssd_16x16_avx2 (1.08%)
- x264_8_pixel_sad_x3_8x8_avx512 (1.06%)
- x264_8_pixel_satd_4x4_avx512 (0.86%)
- x264_8_pixel_ssd_8x8_avx (0.81%)
- mb_mc_01xywh (0.80%)
- x264_8_mb_predict_mv_direct16x16 (0.70%)
- x264_8_pixel_sad_8x8_avx512 (0.62%)
- mb_analyse_inter_b8x8_mixed_ref (0.54%)
- mb_analyse_inter_b16x16 (0.51%)
- x264_8_pixel_satd_16x16_avx512 (0.25%)
- x264_8_pixel_sad_x4_8x16_avx512 (0.23%)
- x264_8_mb_mc (0.26%)
- mc_luma_sse2 (0.24%)
- x264_8_prefetch_fenc_420_mmx2 (0.22%)
- x264_8_pixel_avg_weight_w8_avx512 (0.18%)
- x264_8_mc_offsetsub_w8_mmx2 (0.17%)
- x264_8_mc_offsetsub_w16_sse2 (0.17%)
- x264_8_pixel_satd_4x8_avx512 (0.12%)
- x264_8_pixel_sad_8x16_avx512 (0.14%)
- mb_analyse_inter_direct (0.37%)
- mb_analyse_inter_p8x8_mixed_ref (0.34%)
- mb_analyse_inter_p16x16 (0.16%)
- mb_load_mv_direct8x8 (0.19%)
- x264_8_mb_predict_mv_16x16 (0.30%)
- mb_mc_0xywh (0.30%)
- Total: 0.33 + 4.90 + 4.75 + 4.34 + 3.70 + 3.69 + 3.66 + 3.42 + 3.26 + 2.99 + 1.12 + 0.87 + 1.70 + 1.60 + 0.81 + 0.34 + 1.27 + 1.26 + 0.61 + 1.16 + 1.14 + 1.10 + 1.08 + 1.06 + 0.86 + 0.81 + 0.80 + 0.70 + 0.62 + 0.54 + 0.51 + 0.25 + 0.23 + 0.26 + 0.24 + 0.22 + 0.18 + 0.17 + 0.17 + 0.12 + 0.14 + 0.37 + 0.34 + 0.16 + 0.19 + 0.30 + 0.30 = 56.95%

### Step 4: Ranking the Modules
Based on the aggregated overhead percentages, here is the ranking of the modules by CPU cycle usage:
1. Motion Estimation: 56.95%
  1. Dominant due to extensive motion vector search, subpixel refinement, and SAD/SATD calculations for 76 P-frames and 222 B-frames (298/300 frames).
  2. Key functions: x264_8_me_search_ref (4.90%), get_ref_avx2 (4.75%), refine_subpel (4.34%), x264_8_pixel_satd_8x8_internal_avx512 (3.70%), x264_8_pixel_sad_x4_16x16_avx512 (3.69%).
2. Transform: 8.62%
  1. Significant due to DCT, quantization, and Hadamard transforms for non-skipped macroblocks (~9,955 in P-frames, ~12,573 in B-frames, 792 in I-frames).
  2. Key functions: x264_8_hadamard_ac_8x8_avx2 (1.91%), x264_8_quant_4x4x4_avx2 (1.20%), x264_8_dct4x4x4_internal_avx512 (0.90%).
3. Entropy Coding: 6.76%
  1. Moderate due to CABAC encoding, especially for I-frames (13.9 KB) and trellis quantization.
  2. Key functions: x264_8_cabac_block_residual_rd_internal_avx512 (0.90%), cabac_mvd (0.85% + 0.72%), x264_8_trellis_cabac_4x4_ssse3 (0.70%).
4. Intra Prediction: 2.22%
  1. Lowest due to minimal I-frame usage (2 I-frames, 792 macroblocks total).
  2. Key functions: slicetype_mb_cost (0.87%, shared), x264_8_intra_satd_x9_4x4_avx (0.26%), x264_8_intra_satd_x3_8x8c_ssse3 (0.23%).

### Step 5: Estimating Absolute Cycle Counts
The perf_report.txt indicates an approximate total of 3,104,072,026 cycles over ~0.213 seconds (from your x264 log, 300 frames encoded at 1410.88 fps). Using the percentages, we can estimate the cycles per module:
- Total Cycles: 3,104,072,026
- Motion Estimation: 56.95% × 3,104,072,026 ≈ 1,767,769,039 cycles
- Transform: 8.62% × 3,104,072,026 ≈ 267,571,009 cycles
- Entropy Coding: 6.76% × 3,104,072,026 ≈ 209,835,269 cycles
- Intra Prediction: 2.22% × 3,104,072,026 ≈ 68,910,398 cycles
To verify the total cycles, we can estimate based on CPU frequency:
- Command: Run lscpu | grep "CPU MHz" to get the CPU frequency.
- Example: If the CPU is 3 GHz (3×10^9 cycles/second), cycles ≈ 0.213 seconds × 3×10^9 = 639,000,000 cycles. This is lower than the reported 3.1 billion, suggesting a higher effective frequency (e.g., turbo boost) or multi-core execution. Please share the CPU frequency for a precise calculation.

### Step 6: Validation with x264 Log
The ranking aligns with the x264 log:
- Motion Estimation: Dominant due to 298 P/B-frames, with medium preset settings (--me hex, --subme 7, multiple reference frames) and non-skipped macroblocks (~9,955 in P-frames, ~12,573 in B-frames). The high cycle count (56.95%) reflects the computational complexity of motion search and subpixel refinement.
- Transform: Moderate usage (8.62%) due to 8x8 transforms (51.2% inter, 65% intra) and non-skipped macroblocks.
- Entropy Coding: Moderate (6.76%) due to CABAC, with peaks for I-frames (13.9 KB) but lower impact for small P/B-frames (1.1 KB, 107 bytes).
- Intra Prediction: Low (2.22%) due to only 2 I-frames and minimal intra macroblocks in P-frames (0.1%).

### Step 7: Addressing Kernel Symbol Restriction Warning
The [unknown] [k] entries (e.g., 0xffffffff82600124, 0xffffffff8258d894) indicate restricted kernel symbol resolution due to /proc/sys/kernel/kptr_restrict. These don’t affect user-space x264 profiling, as most cycles are attributed to x264 functions. To resolve for completeness:
1. Check Settings:
  bash
  Copy
  cat /proc/sys/kernel/kptr_restrict cat /proc/sys/kernel/perf_event_paranoid
2. Run as Root:
  bash
  Copy
  sudo perf record -e cycles -g ./x264 --log-level debug --preset medium --crf 23 --output output.h264 input.y4m sudo perf report -n --stdio > perf_report_root.txt
3. Adjust Settings:
  bash
  Copy
  sudo sysctl -w kernel.kptr_restrict=0 sudo sysctl -w kernel.perf_event_paranoid=1
  Then rerun perf record.
Since Motion Estimation dominates, the user-space data is sufficient, and rerunning isn’t necessary unless you need kernel details.

### Step 8: Optimizing the Most Cycle-Intensive Module
Motion Estimation (56.95%) is the most cycle-intensive module. To reduce its cycle usage, consider the following optimizations (trade-offs may affect quality or bitrate):
1. Simplify Motion Search:
  1. Use a faster search algorithm: --me dia (diamond search) instead of --me hex (hexagonal).
  2. Command:
    bash
    Copy
    ./x264 --log-level debug --preset medium --me dia --crf 23 --output output.h264 input.y4m
2. Reduce Subpixel Refinement:
  1. Lower subpixel motion estimation: --subme 1 (faster) instead of --subme 7.
  2. Command:
    bash
    Copy
    ./x264 --log-level debug --preset medium --subme 1 --crf 23 --output output.h264 input.y4m
3. Limit Reference Frames:
  1. Reduce the number of reference frames: --ref 1 instead of the default (likely 3-5 in medium preset).
  2. Command:
    bash
    Copy
    ./x264 --log-level debug --preset medium --ref 1 --crf 23 --output output.h264 input.y4m
4. Combined Optimization:
  bash
  Copy
  ./x264 --log-level debug --preset medium --me dia --subme 1 --ref 1 --crf 23 --output output.h264 input.y4m
  1. Monitor the impact on bitrate (may increase) and quality (may decrease slightly).

### Step 9: Final Answer
Based on the perf_report.txt analysis, the x264 modules rank as follows by CPU cycle usage:
1. Motion Estimation: 56.95% (~1,767,769,039 cycles)
2. Transform: 8.62% (~267,571,009 cycles)
3. Entropy Coding: 6.76% (~209,835,269 cycles)
4. Intra Prediction: 2.22% (~68,910,398 cycles)
Most Cycle-Intensive Module: Motion Estimation, consuming 56.95% of CPU cycles, primarily due to motion vector search (x264_8_me_search_ref, 4.90%), reference frame access (get_ref_avx2, 4.75%), and subpixel refinement (refine_subpel, 4.34%).

### Step 10: Next Steps and Questions
1. Share CPU Frequency: Run lscpu | grep "CPU MHz" to confirm the total cycle estimate.
2. Optimization: Do you want to test the suggested Motion Estimation optimizations (e.g., --me dia, --subme 1)? I can guide you through comparing performance and quality.
3. Further Analysis:
  1. Want to visualize the data with a flame graph? Install hotspot:
    bash
    Copy
    sudo apt install hotspot hotspot perf.data
  2. Need a deeper dive into specific functions or module sub-components?
4. Kernel Warning: Should we rerun perf record as root to resolve [unknown] [k] entries?
Please let me know your CPU frequency, any optimization preferences, or additional details (e.g., video content type—static or high motion), and I’ll refine the analysis or assist further!