Intrinsics (also called intrinsic functions) are special functions provided by compilers that map directly to specific CPU instructions, typically SIMD (Single Instruction, Multiple Data) or low-level machine instructions. They allow you to optimize performance by writing C/C++ code that takes advantage of CPU-specific features like vectorization, parallelism, and bit manipulation—without writing full assembly code.

### Types of Intrinsics (by CPU Instruction Sets)
Type	Description
MMX	Early SIMD for multimedia; obsolete on modern systems
SSE / SSE2/3/4	Streaming SIMD Extensions; 128-bit wide vector operations
AVX / AVX2	Advanced Vector Extensions; 256-bit wide operations
AVX-512	512-bit SIMD; used in HPC and AI workloads
NEON (ARM)	SIMD for ARM processors (used in mobile and embedded)
BMI / BMI2	Bit Manipulation Instructions for efficient bit-level processing
FMA	Fused Multiply-Add for reduced rounding and speed (e.g., a*b + c in one)
AES-NI	Hardware acceleration for AES encryption
SHA Intrinsics	Hardware support for SHA hash algorithms (e.g., SHA-1, SHA-256)

### Intrinsics Headers (x86)
Header File	Used For
mmintrin.h	MMX
xmmintrin.h	SSE
emmintrin.h	SSE2
pmmintrin.h	SSE3
tmmintrin.h	SSSE3
smmintrin.h	SSE4.1
nmmintrin.h	SSE4.2
immintrin.h	AVX, AVX2, AVX-512, FMA, etc.
arm_neon.h (ARM)	ARM NEON intrinsics

x264/encoder/analyse.c
optimize-analyse_update_cache()

static void analyse_update_cache( x264_t *h, x264_mb_analysis_t *a )
{
    switch( h->mb.i_type )
    {
        case I_4x4:
        for( int i = 0; i < 16; i++ )
        {
        //h->mb.cache.intra4x4_pred_mode[x264_scan8[i]] = a->i_predict4x4[i];
        // If x264_scan8[i] == i for i=0..15, you can do:
        __m128i v = _mm_loadu_si128((__m128i*)a->i_predict4x4);
        _mm_storeu_si128((__m128i*)&h->mb.cache.intra4x4_pred_mode[x264_scan8[0]], v);
        }
        mb_analyse_intra_chroma( h, a );
        break;

------------------------------------------------------------------------------------------------------------------------
Let’s compute the relative improvement in analyse_update_cache:
Improvement=1.221.22−0.88​×100≈27.87%
So your SIMD optimization reduced the CPU time of this function by ~28%.
### Optimization Gain:
Let’s compute the relative improvement in analyse_update_cache:
Improvement=1.221.22−0.88​×100≈27.87%
So your SIMD optimization reduced the CPU time of this function by ~28%.

### Step 1: Understanding the 4x4 Block Structure
A 16x16 macroblock contains 256 pixels, divided into 16 4x4 blocks (each with 16 pixels), as shown in your diagram:

The 16x16 macroblock is divided as follows:

+-------+-------+-------+-------+
| 4x4 B1| 4x4 B2| 4x4 B3| 4x4 B4|
+-------+-------+-------+-------+
| 4x4 B5| 4x4 B6| 4x4 B7| 4x4 B8|
+-------+-------+-------+-------+
| 4x4 B9| 4x4 B10|4x4 B11|4x4 B12|
+-------+-------+-------+-------+
| 4x4 B13|4x4 B14|4x4 B15|4x4 B16|
+-------+-------+-------+-------+

Each 4x4 block contains 16 pixels.
[P(0,0), P(0,1), P(0,2), P(0,3)]
[P(1,0), P(1,1), P(1,2), P(1,3)]
[P(2,0), P(2,1), P(2,2), P(2,3)]
[P(3,0), P(3,1), P(3,2), P(3,3)]

For a 16x16 macroblock divided into 16 4x4 blocks, each 4x4 block can be predicted using one of nine intra prediction modes (Intra_4x4).
Each 4x4 block (e.g., B1, B2, ..., B16) is processed independently for intra prediction.
The blocks are typically processed in raster scan order (left-to-right, top-to-bottom): B1, B2, B3, B4, B5, ..., B16.

### Step 2: Intra Prediction Modes for 4x4 Blocks
H.264 defines nine intra prediction modes for 4x4 luma blocks (Intra_4x4). These modes predict the 16 pixels in a 4x4 block using neighboring pixels from adjacent blocks (top, left, or both). The modes are:
1. Mode 0 (Vertical): Predicts pixels by copying values from the 4 pixels above the block.
2. Mode 1 (Horizontal): Predicts pixels by copying values from the 4 pixels to the left.
3. Mode 2 (DC): Predicts pixels using the average of available pixels from above and left (or a fixed value if neighbors are unavailable).
4. Mode 3 (Diagonal Down-Left): Predicts along a 45° angle from top-right to bottom-left.
5. Mode 4 (Diagonal Down-Right): Predicts along a 45° angle from top-left to bottom-right.
6. Mode 5 (Vertical-Right): Predicts along a vertical-right angle.
7. Mode 6 (Horizontal-Down): Predicts along a horizontal-down angle.
8. Mode 7 (Vertical-Left): Predicts along a vertical-left angle.
9. Mode 8 (Horizontal-Up): Predicts along a horizontal-up angle.
Each mode corresponds to a directional pattern or a simple averaging (DC) method, based on the assumption that pixel values are consistent along certain directions.
Suppose the analysis phase determined the following intra prediction modes for the 16 4x4 blocks:
- a->i_predict4x4[] = [0, 1, 2, 3, 0, 2, 1, 4, 2, 8, 7, 6, 1, 2, 0, 2] (e.g., 0=Vertical, 1=Horizontal, 2=DC, etc.).
- The x264_scan8 array might map indices like:
  - x264_scan8[0] = 0 (B1), x264_scan8[1] = 1 (B2), x264_scan8[4] = 8 (B5), etc., depending on x264’s internal ordering.
The loop copies each mode to the cache:
- For i=0: h->mb.cache.intra4x4_pred_mode[x264_scan8[0]] = a->i_predict4x4[0] (e.g., mode 0 to B1’s cache position).
- For i=1: h->mb.cache.intra4x4_pred_mode[x264_scan8[1]] = a->i_predict4x4[1] (e.g., mode 1 to B2’s position).
- And so on, up to i=15.
After the loop, h->mb.cache.intra4x4_pred_mode contains all 16 modes in the correct order for encoding.

Prepared to encode the macroblock by storing modes in the cache for:
  1. Computing residuals (actual pixels minus predicted pixels).
  2. Signaling modes to the decoder (using Most Probable Mode to reduce bits).
  3. Providing neighbor data for subsequent blocks or macroblocks.

The optimization comes from using SSE intrinsics (_mm_loadu_si128 and _mm_extract_epi8) to process multiple data elements in parallel. Here’s a detailed breakdown:
#### 1. SIMD Data Loading with _mm_loadu_si128

__m128i data = _mm_loadu_si128((__m128i*)a->i_predict4x4);

What It Does:
_mm_loadu_si128 loads 16 bytes (128 bits) from the memory address a->i_predict4x4 into a 128-bit SIMD register (__m128i).
In x264, a->i_predict4x4 is an array of 16 uint8_t values (each representing an intra prediction mode, 0–8, for one of the 16 4x4 blocks).
This instruction loads all 16 modes into a single __m128i register in one operation, rather than accessing each uint8_t individually as in the scalar loop.

Optimization:
- Single Memory Access: The scalar loop requires 16 separate memory reads to access a->i_predict4x4[i] for i=0 to 15. In contrast, _mm_loadu_si128 performs one memory read to load all 16 bytes, reducing memory access overhead.
- Unaligned Load: The u in _mm_loadu_si128 indicates an unaligned load, meaning the memory address doesn’t need to be 16-byte aligned. This makes the code more flexible, as a->i_predict4x4 may not be aligned in memory, but it’s slightly slower than an aligned load (_mm_load_si128).
- Vectorization: The 16 modes are now in a single 128-bit register, ready for vectorized processing (though the loop still extracts them individually in this case).

#### Extracting Bytes with _mm_extract_epi8
- Instruction:
  uint8_t v = _mm_extract_epi8(data, i);
- What It Does:
  - _mm_extract_epi8 extracts a single 8-bit value (one intra prediction mode) from the __m128i register data at index i (0 to 15).
  - The extracted value v is assigned to h->mb.cache.intra4x4_pred_mode[x264_scan8[i]], mapping it to the correct position in the cache.

Optimization:
- Vector Register Access: The modes are already loaded into the data register, so _mm_extract_epi8 accesses data from the register rather than memory, which is faster.
- Potential for Further Vectorization: While this loop extracts one byte at a time, the use of __m128i sets the stage for further SIMD optimizations (e.g., vectorized writes or processing), though the current code doesn’t fully exploit this.

Why Still a Loop?:
- The x264_scan8 array introduces a non-sequential memory access pattern because it maps linear indices (0–15) to specific positions in h->mb.cache.intra4x4_pred_mode (e.g., accounting for H.264’s block ordering).
- This non-sequential access prevents a fully vectorized write (e.g., using _mm_storeu_si128) to the cache, as the destination addresses are scattered.
- Thus, the loop extracts each mode individually with _mm_extract_epi8 and writes it to the mapped position.

#### Overall Performance Gains
- Memory Access:
  - Scalar Loop: 16 memory reads for a->i_predict4x4[i] and 16 memory writes for h->mb.cache.intra4x4_pred_mode[x264_scan8[i]].
  - SIMD Version: 1 memory read (_mm_loadu_si128) for all 16 modes, plus 16 memory writes (same as scalar due to scattered access).
  - Gain: Reduces memory read operations significantly, which is critical because memory accesses are slower than register operations.
- Instruction Efficiency:
  - _mm_loadu_si128 is a single instruction that loads 16 bytes, faster than 16 scalar reads.
  - _mm_extract_epi8 (available in SSE4.1 or later) is a fast register operation to extract one byte from the __m128i register.

In scalar loop what happen we read from memory 16 times and write to the memory 16 times
but in simd we read memory 1 time and write to the memory 16 times.

The code:
__m128i data = _mm_loadu_si128((__m128i*)a->i_predict4x4); for (int i = 0; i < 16; i++) { uint8_t v = _mm_extract_epi8(data, i); h->mb.cache.intra4x4_pred_mode[x264_scan8[i]] = v; }
short way:-
What it does: Copies 16 intra 4x4 prediction modes (0–8) for a 16x16 macroblock’s 4x4 blocks from a->i_predict4x4 to h->mb.cache.intra4x4_pred_mode using x264_scan8 mapping.
Optimization:
- Uses SSE SIMD:
  - _mm_loadu_si128: Loads all 16 modes in one memory read (vs. 16 in scalar loop).
  - _mm_extract_epi8: Extracts each mode from a 128-bit register, faster than memory access.
- Benefit: Reduces memory reads from 16 to 1, saving bandwidth and cycles.
- Limitation: Loop remains due to scattered writes (x264_scan8), preventing full vectorization.
Impact: Speeds up x264 encoding by minimizing memory access for mode caching.

-----------------------------------------------------------------------------------------------------------------------
writeen in assembly lang so rewritten in c using avx512 older used x264_8_pixel_avg2_w16_sse2
x264/common/pixel.c

#if !HIGH_BIT_DEPTH
void x264_8_pixel_avg2_w16_avx512(uint8_t *dst, int dst_stride,
        uint8_t *src1, int src1_stride,
        uint8_t *src2, int src2_stride,
        int width, int height)
{
    fprintf(stderr, "Called x264_8_pixel_avg2_w16_avx512\n");
    for (int y = 0; y < height; y++)
    {
        __m512i s1 = _mm512_loadu_si512((__m512i*)src1);
        __m512i s2 = _mm512_loadu_si512((__m512i*)src2);
        __m512i avg = _mm512_avg_epu8(s1, s2);
        _mm512_storeu_si512((__m512i*)dst, avg);
        dst += dst_stride;
        src1 += src1_stride;
        src2 += src2_stride;
    }
}
#endif /* !HIGH_BIT_DEPTH */

--------------------------------------------
register
-----------------------------------------------
if( cpu&X264_CPU_AVX512 )
    {
        INIT8( sad, _avx512 );
        INIT8_NAME( sad_aligned, sad, _avx512 );
        INIT7( sad_x3, _avx512 );
        INIT7( sad_x4, _avx512 );
        INIT8( satd, _avx512 );
        INIT7( satd_x3, _avx512 );
        INIT7( satd_x4, _avx512 );
        pixf->sa8d[PIXEL_8x8] = x264_pixel_sa8d_8x8_avx512;
        pixf->var[PIXEL_8x8] = x264_pixel_var_8x8_avx512;
        pixf->var[PIXEL_8x16] = x264_pixel_var_8x16_avx512;
        pixf->var[PIXEL_16x16] = x264_pixel_var_16x16_avx512;
        pixf->var2[PIXEL_8x8] = x264_pixel_var2_8x8_avx512;
        pixf->var2[PIXEL_8x16] = x264_pixel_var2_8x16_avx512;
        pixf->avg2[PIXEL_16x16] = x264_8_pixel_avg2_w16_avx512;
        fprintf(stderr, "Forced avg[16x16] to x264_8_pixel_avg2_w16_avx512\n");
        // Force a test call
    uint8_t dummy1[64] = {0}, dummy2[64] = {0}, dummy_dst[64] = {0};
    x264_8_pixel_avg2_w16_avx512(dummy_dst, 16, dummy1, 16, dummy2, 16, 16, 4);

    }

----------------------------------------------------------------------------------------------------------------------